Lazarus

Configurable Highlighter for SynEdit
TSynFacilSyn 1.20

TECHNICAL
AUTHOR	Tito Hinostroza - Lima Peru
DATE	23/04/2017 terminated Rev1
APPLICABLE TO	SynEdit Package of Lazarus 1.6 / Examples have been developed on Windows-32.
LEVEL DOCUMENT	Medium-High. Knowledge of Free Pascal, Lazarus and SynEdit is assumed.
PREVIOUS DOCUMENTS	We suggest reading "The Bible of SynEdit".
TRANSLATION	Tim Sinaeve, Tito Hinostroza

NOTES FOR VERSION 1.20

This version overcomes, at least in part, the limitation of not being able to create sections within blocks. Currently, it is allowed to create an additional definition of the section within another section, but does not allow a higher level of nesting.

All other performance characteristics and parameters are maintained.

# Introduction

The TSynFacilSyn highlighter, for SynEdit component, is similar to the Lazarus highlighter SynAnySyn, but it's more efficient and configurable. All this highlighter code is defined in a single unit.

The TSynFacilSyn highlighter can read a complete syntax defined in an external file. This file syntax specifies the working mode to use for the highlight. A syntax file is an XML file that defines a single language. If you want to have different languages, you must have different XML, one for each language.

Also You can configure the syntax highlighter, by code, using the methods of "TSynFacilSyn" class.

The TSynFacilSyn highlighter SynEdit only work with Lazarus component. Implements syntax highlighting and code folding.
### Characteristics

- It is configurable. Design a syntax highlighting, using an external XML file or using code instructions.
- It is fast and consumes low memory. It is optimized to be comparable in speed to a non-configurable highlighter.
- Allows you to easily configure most syntax elements such as identifiers, strings, numbers and comments in a way that it adapts to most languages.
- It is oriented towards the management of tokens and attributes. Each token contains a single attribute.
- Allows definition of the characters that are valid for identifiers so it can be adapted to the specific definition of each language.
- It can handle subsets of identifiers (reserved words, variables, directives, etc.) and subsets of symbols (operators, separators, etc.).
- Supports multi-line comments and strings.
- Can create new tokens, using identifiers as delimiters (similar to blocks << Heredoc).
- Includes "CaseSensitive" property.
- Define blocks with or without code folding. Includes several options to suit most programming languages.
- You can color the background of the blocks.
- The XML syntax file allows simplified ways to define tokens.
- Manages several predefined attributes but they can be used more dynamically.

# Summary
## Use within a program.

This highlighter consists of a single sourcefile: "SynFacilHighlighter.pas". You must include this file in the folder where the work project or folder of the project units is.

Once copied, the unit must be included in the USES statement in units which will use the highlighter.

As with any highlighter, we must create an instance of the highlighter (TSynFacilSyn) and assign it to the editor that we will use:

uses ..., SynFacilHighlighter;

var
    hlt : TSynFacilSyn;

...
  hlt : = TSynFacilSyn.Create(self); //creates highlighter
  editor.Highlighter : = hlt;
  hlt.LoadFromFile('SynPHP.xml'); //Load file syntax
...
  htl.Free; //Free

To use the highlighter, you must first configure the syntax. This can be done using an external file (syntax) or by code.

## Configuration using syntax file

For example, if we want a simple syntax of PHP files, we could create an XML file and put this content:

<Language name="Php">
  <String Start="'" End="'"> </String>
  <String Start="&quot;" End="&quot;" > </String>
  <Comment Start="//" > </Comment>
  <Comment Start="/*" End="*/" > </Comment>
  <Keyword>
__file__ __LINE__ array and break case class const continue default do doublé die echo empty endfor endif elseif else endswitch endwhile eval exit extends false float for global function highlight_file highlight_string int integer if isset include new object list old_function actual print or return show_source require static string unset var switch while true xor
  </Keyword>
</Language>

Then we should use the LoadFromFile() method to set the highlighter to this file.

## Configuration using Code

The syntax can also be set using code instead of an external file. This gives us greater flexibility but requires more care. The following code to define the syntax of the XML file shown above:

  hlt1.ClearMethodTables;
  hlt1.ClearSpecials;
  hlt1.DefTokIdentif('[$A-Za-z_]', '[A-Za-z0-9_]*');

  hlt1.AddKeyword('__file__ ');
  hlt1.AddKeyword('__LINE__');
  hlt1.AddKeyword('array');
  hlt1.AddKeyword('and');
...
  hlt1.AddKeyword('while');
  hlt1.AddKeyword('xor');

  hlt1.DefTokDelim('''','''', hl.tnString);
  hlt1.DefTokDelim('"','"', hl.tnString);
  hlt1.DefTokDelim('//','', hl.tnComment);
  hlt1.DefTokDelim('/\*', '\*/', hl.tnComment, tdMulLin, true);
  hlt1.Rebuild;

## Changing attributes

The attributes can be changed in the XML file or using code.

The following XML file shows how the properties of the attributes are defined:

<Language name="Oracle SQL" ext="Psql" ColorBlock="Block">
  <Attribute Name="Keyword" ForeCol="#40A040" Bold="False" Backcol="#404040">
  </Attribute>
  <Attribute Name="Number" FrameCol="#4040A0" Italic="True" Strikeout="True">
  </Attribute>

...

</Language>

For more information about setting attributes see section 4.3 - Setting attributes

To change the attributes in code should access the properties of attributes:

  //Load syntax
  hlt : = TSynFacilSyn.Create(self);
  hlt.LoadFromFile('SynPHP.xml');
  //change the text color Keywords
  hlt.tkKeyword.Foreground : =clGray;
  //change the background color of the chains
  hlt.tkString.Background : =clyellow;
  //change the text color of comments
  hlt.tkComment.Foreground : =clRed;

There are several predefined attributes highlighter, but it's only needed to set what we are going to use.

Some attributes have default properties set, as keywords and comments.
## Code folding

The highlighter TSynFacilSyn has built in configurable support for code folding:

Code folding can be enabled for multi-line tokens or for blocks containing several tokens.

Folding strings like in the example are defined in XML as follows:

  <Start String="&quot;" End="&quot;" Folding="True"></String>

To define folding blocks delimited by tokens, you can use the following definition:

  <Start Block="BEGIN" End="END" Folding="True"></Block>

The folding can be configured both, by syntax file and by code. Later it's indicated how to enable the folding.

# Understanding the syntax

## Syntax elements

Syntax may be specified for different levels. We know that a low level, the languages are just a set of character, or even on a lower level languages, they are single set of bytes (or bits).

Consider a simple sequence of a programming language:

Note that the correspondence between bytes and characters is not always one to one as it depends on the encoding scheme. In this case, SynEdit uses UTF-8 encoding which means characters can be up to 4 byte in length. Furthermore tabs that are represented as one byte while they can occupy several character places on screen.

The TSynFacilSyn highlighter processes the characters as if they were single bytes. Accented characters are processed as two characters (because actually stored as two bytes in UTF-8).
You need to know two key concepts to understand the functioning of highlighter TSynFacilSyn:

A token is one or more characters grouped by specific rules. Each token corresponds to one and only one attribute, which may have a different color or background.

Attributes are properties of highlighter that can be applied to a particular token. In SynEdit, an attribute is represented by an instance of the "TSynHighlighterAttributes" class and is used to define properties such as text color, background color, font, or font style.

Strings and comments are always treated as a single token and have a unique attribute.

Tokens of type "string"

          A highlighter is somehow a lexical analyzer (lexer) that analyzes text and identifies "tokens," which are lexical terms of a language[1].
            [1] Above the lexical level, is the syntactic and semantic level. Usually highlighting is not influenced by these levels, except in special cases where it can be important (as in the case of the keywords.)

Tokens are classified into various types into the highlighter[2]. New types can be created dynamically, but there are 8 pre-defined types:
[2] Other highlighters in Lazarus can handle other types of tokens.

1. End of line
2. Symbols
3. Spaces
4. Identifiers
5. Numbers
6. Keywords
7. Strings
8. Comments

These types of tokens exist for every highlighter and meet the basic needs of simple highlighters.

The other types of tokens like variables, constants, functions, procedures, types, etc. must be created before use within the highlighter. Section 4 and 5 discusses how you can create additional types of tokens.

When the highlighter is linked to the text editor, all tokens are associated to any of the existing types:

  cad = "hello world"
//comment

tnEol

tnSymbol

tnIdentif

tnNumber

tnKeyword

tnString

tnComment

tnSpace

TOKEN TYPE

A token can only belong to one type of token.

The different token types are identified by an ID in the highlighter:

   tnEol : integer; //id for tokens newline
   tnSymbol : integer; //id for symbols
   tnSpace : integer; //id for spaces
   tnIdentif : integer; //id for identifiers
   tnNumber : integer; //id for numbers
   tnKeyword : integer; //id for keywords
   tnString : integer; //id for strings
   tnComment : integer; //id for comments

In addition, for each identifier, it has an associated attribute:

    //Predefined Attributes
    tkEol : TSynHighlighterAttributes;
    tkSymbol : TSynHighlighterAttributes;
    tkSpace : TSynHighlighterAttributes;
    tkIdentif : TSynHighlighterAttributes;
    tkNumber : TSynHighlighterAttributes;
    tkKeyword : TSynHighlighterAttributes;
    tkString : TSynHighlighterAttributes;
    tkComment : TSynHighlighterAttributes;

The ID identifies a token within the highlighter, while the attribute let us define the visual appearance of the token.

Unlike existing highlighters in Lazarus, in TSynFacilSyn there are not enumerated variables to identify the token types. It's used an integer number.

We need to know which type a token has, in order to associated it with the corresponding attribute.

The rule is that each token type, is associated with a single attribute, as shown in the following diagram:

 cad = "hello world"
//comment

tnNull

tnSymbol

tnIdentif

tnNumber

tnKeyword

tnString

tnComment

tnSpace

tkIdentif

tkSymbol

tkSpace

tkNumber

tkKeyword

tkString

tkComment
TOKEN TYPE
ATTRIBUTE

NIL

The pre-defined types of tokens are listed in the following table:

ATTRIBUTE TYPE	NAME IN CODE	NAME IN XML	DESCRIPTION
End of line	tnEol	EOL	Used to detect the end of line. It has a fixed definition and can not be changed.
Symbol	tnSymbol	SYMBOL	Represents the symbols that are not identifiers, numbers, spaces, strings or any other token type.
Whitespace	tnSpace	SPACE	Represents non-printable characters in a language. Includes line breaks and control characters. It has a fixed definition and can not be changed.
Identifier	tnIdentif	IDENTIFIER	Represent identifiers in language. These identifiers can be names of variables, functions, etc.
Numbers	tnNumber	NUMBER	Represents numeric constants in a language such as 99, 0243, 0xA0, $FF
Keyword	tnKeyword	KEYWORD	They are special identifiers. Usually represents the reserved words in a language, such as FOR, BEGIN, RETURN.
String	tnString	STRING	Represents to string constants used in most languages, such as "hello", "world".
Comments	tnComment	COMMENT	Represents the comments within the code of a program.

The keyword category has been created to apply to certain types of identifiers, called "Special Identifiers". Thus formally we could have defined them as sub-identifiers, but here they are defined separately to support a wider range of languages. In some languages there can be totally different syntactic elements like variables in PHP, which can be identified as special tokens because they start with $.

The amount of different types of tokens (attributes available) indicates the number of different visual features that can be applied to various elements of the text of a syntax. When the predefined types are not enough, custom token types can be created.

An attribute is usually associated to a similar type of element in a language, ie number attributes that apply to the numbers (numeric constants) of a language. The TSynFacilSyn highlighter is so flexibile, that could apply the numbers attribute to identifiers or even strings.

To be precise, we must assume that the highlighter always applies the attributes corresponding to each token type. Tokens can be defined in different ways, without following the provisions. Ie, we could define the token “123” like a Symbol Token, when it's expected to be a Number Token.

### Identifiers

An identifier is a character string, usually alphanumeric and usually starting with a letter or symbol and followed by any letters, numbers or symbols.

Each language has its own identifier naming rules, but generally most of them share the same characteristics such as supporting all alphabetic characters.

Usually, identifiers are considered as a single token, but it is possible to define more extensive delimiter tokens that can be used to interpret the token as an identifier.

### Numbers

In many languages numerical tokens are considered like strings containing numeric digits or some auxiliary character. For example: 5943, 0123, 05, etc.

Also forms like $FF and 0x1A numbers can be supported. In general all numerical constants of a language should fall into the category of numerical tokens.

Each language can allow different characters in numbers, but usually it will be: 0123456789

### Whitespace

Whitespace are any characters with a character code less than #32. This includes real spaces, tabs, control characters, etc.

Any string of whitespace characters are considered as a single whitespace token.

For example the following strings wille be interpreted are whitespace tokens:

' '
#9#32#32
#1#2#3

The characters considered as whitespace are fixed in the highlighter and can not be changed. Whitespace tokens can also support attributes but this feature has been disabled for performance reasons. If you want to activate attributes for spaces, you will have to modify the TSynFacilSyn.GetTokenAttribute() method.

Characters #10 and #13 are considered like whitespaces inside the highlighter, but usually they are never processed because they are deleted when the text is loaded in SynEdit.
### Strings

Strings are special tokens that are usually placed between two string delimiters. The string delimiters are usually the quote or apostrophe symbols like "Hello" or 'world'. These are identified in a language like string literals.

There can be defined several types of strings with different delimiters. Usually, the starting and ending delimiters are the same but this is no requirement.

The following example shows a piece of code where we have defined two types of strings delimited by quotation marks and apostrophes:

Some characteristics of string tokens:

- Strings may occupy one or more lines.
- Delimiters are also part of the string token.
- Strings of a single line can contain any characters, including and other strings delimiters (which are ignored).
- Strings can not be nested. A string can not be nested within another string of the same token type.
- Strings are parsed as a single token, except when they occupy more than one line.

This last feature can be explained as follows. Imagine you have a text string which occupies several lines:

Normally the colored area should be interpreted as a single string token, but because of the way SynEdit works (scan by lines), a string token can only occupy a single line. So SynEdit will actually interpret this string as 3 seperate string tokens.
### Comments

Comments are usually tokens placed between two comment delimiters. These delimiters are often symbols which consist of one or more characters.

Several types of comments can be defined with different delimiters. Common types of comments are:

- Single line : occupy a single line. Usually specified by only a starting delimiter which implies that the comment extends to the end of the line.
- Multi-line comments can span multiple lines of text. They usually specified by a start and end delimiter.

Some key features of comments are:

- They can span one single or multiple lines.
- The delimiters are also part of the comment token.
- The single-line comments can contain any characters inside, including delimiters used by other comment token types (which are ignored).
- Comments can not be nested. A comment token can not be placed inside another comment of the same token type.
- Comments consist of a single token, except when they occupy several lines.

### Symbols

Symbols are tokens which are composed of characters that are not part of any other token (strings, comments, identifiers, numbers, etc.).

Usually symbols are no alphanumeric tokens but you can define symbol tokens that contain numeric or alphabetic characters in your syntax definition.

In the following example a language is shown that only recognizes whitespace, so that all other characters (with a light grey background) are interpreted as symbol tokens:

In this other example we have a language that also recognizes identifiers (green background), so that all other characters (with light grey background) are interpreted as symbol tokens:

Like you can see the symbol tokens are formed by all characters that are not part of any other symbol.
## Special identifiers

Usually identifiers are a key element of a syntax definition. They are like the words of a spoken language. As they are usually the most abundant elements, they are often further categorized.

Identifiers may represent variables, constants, functions, policies, types, etc. For example, consider the following elements of the Pascal language:

x	-> Variable (identifier)
VAL_INI	-> Constant (identifier)
TObject	-> Class (Identifier)
Max()	-> Function (identifier with parentheses)

As we see can see, all these language elements are identifiers.

TSynFacilSyn can handle different categories of identifiers, called Special Identifiers. Basically a category is a subset of identifiers which share the same attribute.

As an example consider a piece of code in which there are several identifiers (which all meet the definition of identifiers):

By changing the attribute identifiers, the appearance of all identifiers of the text is changed. But when we know that there are special identifiers, such as keywords, we can identify a sub-set of these identifiers and associate them with any other attribute. These would become then special identifiers.

In our Pascal sample code, we could define the “begin” and “end” identifiers as special identifiers and assign them the attribute of reserved words (KEYWORD).

The special identifiers can be any predefined type KEYWORD, NUMBER, or a custom type.
## Special symbols

At the same way we can define subsets os identifiers to assign a different token type (different from tkIdentif), we can also choose certain combinations of characters (used in symbols), to define special tokens, which may have any other attribute (different from tkSymbol).

These tokens, defined from symbols are called Special Symbols, and can be used to represent special tokens (such as operators or delimiters) in a programming language.

As an example consider a syntax in which defines identifiers (green background) and numbers (orange background):

The grey part represents the symbol tokens. Within these tokens however, we can identify the assignment operator ": =". In this case we can define the token ": =" as a special symbol and assign it to some other attribute.

Special symbols can be the KEYWORD, NUMBER, etc. token types or some custom type.

## Definition of tokens

In TSynFacilSyn, there are two ways to define a token:

BY CONTENT	BY DELIMITER
Are defined by specifying the starting delimiter (one or more characters), and the following characters. / In many languages, they are often used to represent identifiers or numbers. / They cannot be multi-line. / They are referred to as "tokens by content"	Are defined by specifying a starting delimiter (one or more characters) and an end delimiter. / In many languages they are often used to represent strings and comments. / They can be multi-line. / They are referred to as "delimited tokens".

### Tokens by content

When defined by content, the starting delimiter and a set of possible characters for the following characters is always supplied. They have to meet following rules:

- They need to start with a specified initial boundary or start with a character that is in the list of "valid starting characters".
- The successive characters need to be in the "list of valid following characters".

The definition by content is commonly used to define numbers and identifiers (but can be defined some others tokens by content). Following examples show some valid definitions:

<Identifiers CharsStart= "$A..Za..z_" Content = "A..Za..z0..9_"></Identifiers>
<Token CharsStart="0..9" Content = "0..9" Attribute='NUMBER'></Token>
<Token Start="0x" Content = "0..9a..fA..F" Attribute='NUMBER'></Token>

These definitions are recognized because they always include the "Content" field. The content tokens are not multi-line.

### Delimited tokens

When tokens are defined by delimiters, it works with more basic elements called Token delimiters.

The definition by delimiter is common used to define strings and comments, because these items are always delimited by fixed sequences of characters.

A typical definition of a string token type is:

  <Token Start=""" End=""" Attribute="STRING"> </Token>

These definitions are recognized because they always include the parameter "Start". Delimited tokens can be multi-line.

## Token Delimiters

Token delimiters are a set of characters that are used to determine where to begin and/or where a token ends. The tokens for content starting with a delimiter, while delimited tokens will start in and end with a delimiter.

A delimiter is both a complete token. For example, the following are valid delimiters:

{
}
BEGIN
/ *
END
* /
"" "
<! -
REM
#A (Not recommended)

It is not recommended to combine characters of identifiers and symbols in an identifier because it can lead to errors in the interpretation of delimiters due to the way the syntax highlighter component is designed.

The highlighter supports two basic types of delimiters:

- Delimiter identifier. When is a special identifier as BEGIN or END.
- Delimiter symbol. When a special symbol, for example the characters: {}.

The delimiters have the following restriction: if the starting character is an identifier, then all the delimiters must be an identifier. In other words the following list of delimiters are wrong:

REM%
A<
X?X
INI$ (Will only be valid if defined $ as character identifier)

According to its location within a block delimiters can be:

- Of start: the delimiter is indicating the start of a block, for example /*.
- Of end: the delimiter indicates the end of a block, for example */.
- Of Start and end: the delimiter is used for both the start and the end of a block. Examples include the string delimiters.

We can also classify delimiters by their similarity to other delimiters.

- Exclusive: when no other delimiter syntax has any starts with the same characters. For example in the C language, the block delimiter "{" is unique because the character "{" is not included in the string delimiters nor in the comments //, / * and */.
- Inclusive: when there is another delimiter syntax that starts with the same character that starts with this delimiter. This is the case for example with the single line comment delimiter "//" in the C language, whose initial character is also included in the (multi-line) comment delimiter "/*".

This classification is important to optimize the processing of the highlighter syntax. The less exclusive delimiters with syntax, the slower the processing will be done.
## Codeblocks

A powerful feature in this highlighter is the way it can handle code blocks. These not only allow us to create blocks of folding code, but also let us define special regions within the text.

A text block is a logical structure representing a range of text that is enclosed by special tokens (block delimiters).

Consider for example, the following code in C:

void main ()
{
    for (int i = 2; i <= 10; i ++)
    {
        fact = fact * i;
    }
}

The body of the main() function, which is enclosed in braces, can be considered as a block whose delimiters are the characters[3]: {}.
[3] This block is also syntactically the body of the main () function, but a block in the highlighter, need not coincide with syntactic structures of language, although ideally, so be it.

We could also consider the body of the "for" loop as another block, also delimited by braces. This would be a simple case of nested blocks.

Going further, we might consider part of "for", which is in brackets “( … )”, as another block.

The blocks can be single or multiple lines, although it is common that occupy more than one line.

These blocks can be defined within the highlighter as valid blocks. But to what end?

The first utility of the blocks is that they can be folded. This would be the main use of the blocks code in the highlighter. Not all blocks have to be foldable, but usually when using block code are to be foldable.

But, looking a little more utility of blocks, we see that we could make them similar to syntactic blocks of language, so allow us to analyse higher level than simply extracting tokens.

The following rules apply to the blocks:

1. The blocks can be single or multiple lines.
2. Blocks can be nested, but not overlap. An inner block always ends before (or simultaneously) the block containing it.
3. Block delimiters are always tokens. You can not create blocks if their bounding are not clearly defined tokens.
4. The blocks are defined using tokens. Can not begin or end in the middle of a token. Ie always contain a whole number of tokens. This is a consequence of the rule 3.
5. By design issues, the block begins just after the starting delimiter. Ie does not include the initial token.
6. The block extends to the end of the final delimiter. Ie including the end delimiter.
7. The multi-line tokens can not be block delimiters.
8. Building blocks do not affect the structure of tokens. A single block can group consecutive tokens, but will not change its attributes or definitions[4]. The visual appearance of the tokens within a block will not change at all with the block.
  [4] It is planned for future versions that the blocks have some level of influence on the attributes of the tokens it contains.

The process of building blocks will be later described in detail.

## Sections

In addition to the blocks, the TSynFacilSyn highlighter introduces the concept of sections.

A section is a block of code that originates from a starting delimiter, and ends where another section begins or where the block containing it ends.

An example of sections are found in Pascal class definitions:

This code structure presents two clearly defined code blocks, the first is the one that starts with the label "private"; and the other is one that starts with the label "public".

These code blocks are special, because they have a defined boundary. May end when another block (similar or different) starts, or may also be terminated when the main block ends.

To handle such blocks, highlighter implements the concept of "sections". It is not convenient to handle as nested blocks, because they have a slightly different behaviour.

The same rules that apply to blocks, also apply to the "sections", except that:

1. Sections can only be nested once. A section can contain other sections, but these sections cannot contain another sections.
2. A section can contain blocks.
3. A section ends when another section or block, of the same level, begins.
4. A section ends when the block that contains it ends.
5. If a delimiter is delimiter section and block delimiter. His section delimiter feature takes precedence over its block delimiter feature.

Sections usually are enclosed within blocks:

By definition, sections ends before another section begins, or when the block that contains it ends. Thus, the "public" Example section does not include the token "end", which, however, it is part of the block.

Despite the special treatment there, sections are basically blocks. They internally do share the same data structure and only differ by one flag. So when we talk about sections, we often refer to them as blocks.

Creation of sections will be described in detail later.

## Lexical, syntactic and semantic levels

In the analysis of languages, for the purpose of processing by interpreters or compilers, usually separate levels of detail. Generally, the levels usually accept are:

- Lexical: Referred to the identification and removal of tokens of a text, from the characters. Primarily used as the base level for parsing.
- Syntactic.- Use the tokens to form structures according to predefined rules (grammar). They tend to identify more complex elements such as Running, Variable, Constant, expressions, etc.
- Semantic.- It is based on higher level rules applied to a language. Gives meaning to expressions or sentences of the code. A code can be syntactically valid, but be semantically incorrect.

Speaking of a highlighter, usually understood as a machine to identify tokens and to assign attributes of color, background, font, etc.

The highlighter TSynFacilSyn, is designed to be an efficient extractor mechanism for tokens. In this sense it is also what is called a lexical analyser or lexer.

TSynFacilSyn however, goes further because it allows handling code blocks that move in the syntactic level.

If we only use the highlighter to extract tokens, we are definitely moving in the lexical level, but managing blocks of code allows us to come closer to the syntactic level.

Therefore, to define blocks in our language, we must bear in mind not only the folding support we want to give the text but also what these should be according to the syntax of the language which we are working with.

# Configuring Syntax using an external file.

The syntax file is a simple XML file that defines the syntax to use for the highlighter. It can be edited by hand or with a software tool.

It is necessary to ensure that the syntax file in XML, shows no error structure (blocks without closing, invalid characters, etc.), in order to avoid exceptions. Anyway the highlighter does a previous check of the structure of XML, before loading, and raise an exception if it finds any inconsistency.

An exceptions will be raised too, if there is any errors with the syntax definiton, even if the XML file is syntactically correct.

A typical routine to load a syntax code would be:

uses ..., SynFacilHighlighter;

var
    hlt : TSynFacilSyn;

...
  hlt : = TSynFacilSyn.Create(self); //creates highlighter
  editor.Highlighter : = hlt;
  hlt.LoadFromFile('SynPHP.xml'); //Load file syntax
  editor.Invalidate;
...
  htl.Free; //Free

The call to Invalidate() is not necessary if the syntax file is only loaded once. However if it is changed, you need to call Invalidate() to make sure the content suits the new syntax.

It is advisable to include exception handling routines, for errors when loading the syntax file.

## The syntax file

The general structure a file syntax is:

<Language name = "language name" ext = "extension list">
Definition of attributes.
Definition of identifiers and special identifiers.
Definition of symbols and special symbols.
Definition of numbers.
Definition of strings
Definition of comments
Definition of tokens by content.
Definition delimited tokens.
Definition of blocks and sections.
</Language>

No need for all definitions to build a syntax. They can do without majority of configurations and some, are assumed by default.

For example, a simple syntax for PHP could be:

<Language name="Php" ext="Php">
  <Keywords>
array and break case class const continue default do double echo die
endfor endif elseif else endswitch empty eval exit extends endwhile
false float for global function if isset include int integer list
new object old_function actual print or require return show_source
static string unset var switch while true xor
 </Keywords>
</Language>

In this case, the definition of identifiers is not specified, and a default definition is assumed.

This example only defines reserved words in the <Keywords> label. The list of words given can be specified in one or more lines, provided that only spaces or line breaks are used to separate words.

### Special Characters

Like any XML file, the syntax file requires to take into account considerations of characters that can be included.

For special characters in XML are used:

SYMBOL	DESCRIPTION	CODING IN XML
&	Ampersand	&amp;
<	Open angle bracket	&lt;
>	Close angle bracket	&gt;
"	Comilla straight	&quot;
'	Apostrophe	&apos;
	Line break	&#xD;

For example the following statement:

Start = "<"

It is not valid to define a field in XML form. Should be used instead:

Start = "&lt;"

You can also use the form:

&#<ASCII character code>;

So to represent the tab character, type: &#009

The apostrophe can be entered directly, enclosing it in quotes: "'"

To specify blanks, you must enclose the text in quotes: "hello world".

### Using ranges and wildcards

In the syntax file is common to use intervals to avoid typing a long list of characters.

The following intervals are examples of simplified spellings:

A..Z = ABCDEFGHIJKLMNOPQRSTUVWXYZ
a..z = abcdefghijklmnopqrstuvwxyz
0..9 = 0123456789
a..f = abcdef

For example if you want to simplify this statement:

Start = "ABCDEFGHIJKLMNOPQRSTUVWXYZabcdefghijklmnopqrstuvwxyz"

You can use the short form:

Start = "A..Za..z"

There is additionally two predefined wildcards:

%HIGH%	-> ASCII characters from # 128 to # 255 (not implemented)
%ALL%	-> All characters except # 0.

Managing intervals and wildcards are not part of standard XML, but are interpreted by the highlighter own.

### Using simplified forms

Most definitions in the syntax file will be of type:

<token attribute="Attribute_name" value1="XXX" value2="YYY" ... ></token>

To avoid typing too much text, the simplified form is allowed:

<Attribute_name value1="XXX" value2="YYY" ... ></Attribute_name>

This means that the attribute name as a label or marker is used, and thus, it is no longer necessary to specify the attribute.

Another simplified forms, is when you do not want to change the attributes of a label. If such a definition has the form:

<LABEL value1="XXX" value2="YYY" ></LABEL>

If we write the definition in its simplified form:

<LABEL>
</LABEL>

We are indicating that explicitly define the label, but we do not want to change any of its values. This form is useful when the tag is required to create other definitions or to express lists of values ​​(See 4.5.2 - Special Identifiers).

### Using spaces, case sensitive.

Blank spaces and line breaks are ignored in the definition of a language. For example, The following definitions are equivalent:

<LABEL value1="XXX" value2="YYY" > </LABEL>

<LABEL value1="XXX" value2="YYY" >
</LABEL>

<LABEL value1="XXX"
value2="YYY" >
</LABEL>

Although XML is case sensitive by definition, the highlighter is not case sensitive. For example, the following definitions are similar.

<label Value1="XXX" Value2="YYY" >
</label>

<Label value1="XXX" value2="YYY" >
</Label >

<LABEL VALUE1="XXX" VALUE2="YYY" >
</LABEL>

However, by definition of XML, the start and end tag must match the case. The following statement is an error:

<Label Value1="XXX" Value2="YYY" >

</label>

### Colors in the XML file

The colors are defined by typing in #RRGGBB where format:

- RR is the red component in hexadecimal format.
- GG is the green component in hexadecimal format.
- BB is the blue component in hexadecimal format.

For example to define the background of blue as an attribute, use:

 <Attribute Name="Identifier" ForeCol="#0000FF"> </Attribute>

There are however some predefined constants that can be used instead of using this format. Thus, the previous sentence can also be written as:

<Attribute Name="Identifier" ForeCol="Blue"></Attribute>

The constants supported are:

WHITE      =$FFFFFF
SILVER     =$C0C0C0
GRAY       =$808080
BLACK      =$000000
RED        =$FF0000
MAROON     =$800000
YELLOW     =$FFFF00
OLIVE      =$808000
LIME       =$00FF00
GREEN      =$008000
AQUA       =$00FFFF
TEAL       =$008080
BLUE       =$0000FF
NAVY       =$000080
FUCHSIA    =$FF00FF
PURPLE     =$800080
MAGENTA    =$FF00FF
CYAN       =$00FFFF
BLUE VIOLET=$8A2BE2
GOLD       =$FFD700
BROWN      =$A52A2A
CORAL      =$FF7F50
VIOLET     =$EE82EE

### XML Comments

Comments in XML are defined enclosed in delimiters <! - And ->. For example:

<? Xml version="1.0"?>
<!--
This is a comment
-->

Be careful with the combination of characters: --> Or "--"> because they are considered as XML comment delimiter.

## Language Definition

The main tag <Language> supports the following attributes:

Name	Mandatory	Syntax Name
Ext	Optional	List of file extensions associated with the language.
CaseSensitive	Optional	Indicates whether differentiation between uppercase and lowercase apply to locate identifiers and special symbols.
ColorBlock	Optional	Activate the colored blocks. By default it is set to "None". (Off).

There can be only one definition language file.

A minimum definition of typical language would be:

<Language name="Pascal"></Language>

Another definition language could be:

<Language name="Php" ext="php3 php phtml"></Language>

Both examples are empty definitions, but the framework in which all definitions of language must be created.

If the "CaseSensitive" attribute is not specified, it is assumed to be false, ie there will be case-sensitive. To activate, you must assign the string "TRUE":

<Language name="Pascal" ext="pas pp" CaseSensitive="TRUE"></Language>

The "ColorBlock" parameter allows to display blocks with a different background color according to the value it contains. The values ​​that can take are:

"None"	Disables the colored blocks. It is the default option.
"Level"	Color block background by level. Displays the blocks with a more or less dark, according to the level of the block or section color.
"Block"	Block background colors using the color defined for each block, in his "BackCol" parameter. (See Section 4.10 - Block Definition)

The following definition is an example of how to activate the colored blocks by level:

<Language name="Php" ext="Php3 php phtml" ColorBlock="Level"></Language>

For more information about the colored blocks, see Section 4.10 - Block Definition.

It's also possible to include a sample code , using the label <SAMPLE>:

<Language name="Pascal" ext="pas">
<Sample>
  procedure test(var x: byte);
  begin
    x := x +1;
  end;
</Sample>
</Language>

The sample text, can be later accessed from the highlighterm using the property “SampleSource”.

## Setting attributes

The attributes of the tokens, you can configure or create from within the XML file, so you can fully define the look you have each of the categories of tokens within the highlighter.

To set an attribute, the <ATTRIBUTE> is used. For example, to change the appearance of all identifiers of a text, you can use the following definition:

 <Attribute Name="Identifier" ForeCol="#800000" Bold="True"> </Attribute>

This definition shall make all identifiers with red text color and bold. Color parameters must follow the format of three components: #RRGGBB or the name of the color.

If the attribute name already exists, its properties are updated. If the specified attribute does not exist, it first creates the attribute.

The <ATTRIBUTE> tag has the following fields:

Name	Mandatory	Indicates the name of the attribute to be configured.
Backcol	Optional	It is the background color of the token
ForeCol	Optional	It is the color of the text token
FrameCol	Optional	It is the border color of the token
FrameEdg	Optional	Define the scope of turnover token (Around, Bottom, Left or None)
FrameSty	Optional	Is the line type used for (Solid, dashed, Dotted, or Waved) edge.
Bold	Optional	Boolean value. Makes text bold
Italic	Optional	Boolean value. Puts the text in italics
Underline	Optional	Boolean value. Sets the text underlined
Strikeout	Optional	Boolean value. Sets the strikethrough text
Style	Optional	Abbreviated form to specify attributes

They can express multiple definitions of attributes in a syntax file:

<?Xml version="1.0"?>
<Language name="Oracle SQL" ext="Psql" ColorBlock="Block">
  <Attribute Name="Keyword" ForeCol="#40a040" Bold="False">
  </Attribute>
  <Attribute Name="Directive" FrameCol="#4040a0" Italic="True" Strikeout="True">
  </Attribute>
  ...
</Language>

These definitions of attributes may have the following result:

When "FrameCol" parameter is used, the "FrameEdg" parameter allows you to specify where in the edge of the text appears. Its possible values ​​are:

- "Around "-> Full Rim.
- "Bottom "-> Only one line down.
- "Left "-> Just a line to the left.
- "None "-> No border.

The "Style" parameter is a shorthand for the "Bold", "Italic", "Underline" and "strikeout" parameters. It can contain:

b-> Bold text
i -> Text in italics
u> underlined text
s-> strikethrough text

If you want to specify an underlined and bold text, you can use this definition:

  <Attribute Name="Keyword" Style="ub">
  </Attribute>

Do not use the "Bold", "Italic", "Underline" and "strikeout" parameters if "Style" is used.

If the properties of the attributes are not specified, the defaults values are maintained. These default values, usually, do not apply highlighting options, ie, no colors or for text or for the background or for the edge apply. In addition, all attributes are Boolean false.

Most attributes have their properties by default disabled, ie no colors or for text or for the background or for the edge apply. Besides all attributes are boolean false.

However, some attributes have default properties set as keywords and comments. So chains are initially shown with blue text, comments in italics and gray, while the keywords are displayed in green.

A new attribute is created in the same way as an existing attribute is configured. In the following definition, we created the "Specials" attribute and configure two special identifiers in "Specials" attribute:

<?Xml version="1.0"?>
<Language name="Pascal" ext="Pas inc pp" ColorBlock="Level">
  <Attribute Name="Specials" ForeCol="#008000" Bold="True"> </Attribute>
  <Identifiers CharsStart= "A..Za..z_" Content = "A..Za..z0..9_">
    <Specials>
       foo bar
    </Specials>
  </Identifiers>
</Language>

The attribute name is specified in the property "Name =". It can be any length and contain almost any character, but it is recommended that a short name, to improve speed searches.

The name of a new attribute must not be equal to any of the pre-defined attributes in the highlight:

1. EOL
2. SYMBOL
3. SPACE
4. IDENTIFIER
5. NUMBER
6. KEYWORD
7. STRING
8. COMMENT

There is no practical limit to the number of attributes that can be created. It is limited only by the amount of memory available in the system.
## Defining Symbols

Within the highlighter, tokens that will never be absent, are the symbols. This is due to the way the highlighter works internally.

The symbols are the first elements to be defined in a syntax. However, the highlighter makes a default definition, it would be something like this:

<Symbols Content = "%ALL%" ></Symbols>

And this is the first definition applied, and it is expected, that the following definitions will restrict the scope of the symbols.

In fact, the symbol definition excludes white characters #1 .. #31 and #0 null character, for security purposes.

It is not necessary (and not possible) to explicitly define symbols. The highlighter accept the definition of symbols, but not the processing of them. Just accept this definition, allowing define special symbols. So a typical syntax of special symbols, might be:

<Symbols>
  <Token Attribute = "OPERATOR">
  + - * /
  </Token>
</Symbols>

### Special Symbols

Special symbols are defined in the label SYMBOLS:

<Symbols>
  <Operator>
    list of symbols
  </Operator>

  <Delimiter>
    list of symbols
  </Delimiter>

  ...

</Symbols>

Each of these groups may have a different attribute, if it is defined separately.

A common use for special symbols is to define operators:

  <Operators>
    + - * / =
  </Operators>

Here, the used attribute “OPERATOR”, is supposed to be previously defined.

There is no need to put symbols in a specific order. Simply list them separated by spaces or line breaks. The only limitation is that it does not allow the space character to be included as part of a symbol.

The symbols commonly contain alphabetic characters but if needed the comparison shall be made at the CaseSensitive option.

All defined special symbols must be strictly symbols, ie must meet the definition of symbols. For example, you can not define "$$" as a special symbol, if the $ character has been defined as a valid initial character, eg for identifiers.

It is advisable not to include a large number of special symbols, because you can get a deterioration in performance highlighter. The symbol search is not as optimized as seeking special identifiers.

It is important that these lists of special symbols are unique, otherwise an error is generated during loading.

As in the definition of special identifiers, you can also use the "TokPos" parameter to indicate the order in which you must find the token to be considered as a special token.

In the following definition, we specify that the symbol "/" is considered as a special token, only when it appears as the first token of the line.

<Symbols>
  <Special TokPos="1">
    /
  </Special>
  ...

</Symbols>

## Defining identifiers

Identifiers are defined by content by specifying both the initial character and the subsequent characters.

It is defined with the element <Identifiers>.

Attributes include:

CharsStart	Mandatory	List of characters considered valid as the first character of an identifier.
Content	Mandatory	List of characters following characters considered valid as an identifier.

For example a typical definition would be:

<Identifiers CharsStart= "A..Za..z" Content = "A..Za..z0..9_"></Identifiers>

Initial and subsequent characters can be any printable character.

It is important to properly define the characters for an identifier, because the other elements of syntax, as delimiters do depend on this definition.

The characters to use as valid starting characters for identifiers must not conflict with other tokens that are defined by content (such as numbers). If this would be the case the last definition is used or applied by default.

If the definition of identifiers is not specified, a default definition is taken. This is:

<Identifiers CharsStart= "A..Za..z $ _" Content = "A..Za..z0..9_"></Identifiers>

If for some reason, it is wanted to delete the default definition of identifiers, we have to add the following line to your syntax definition:

<Identifiers CharsStart= "" Content = ""></Identifiers>

Identifiers support the definition of subsets of tokens (See 4.5.2 - Special Identifiers).

Do not confuse the definition of identifiers (which are special elements in the highlighter) with the simplified form of tokens for content (see next section).

### UTF-8 Identifiers

The UTF-8 characters like “ñ” are stored as two bytes instead of one. This means it can not be handled directly by the highlighter like single byte characters.

SynFacilSyn allows using UTF-8 characters in the definition of identifiers, but these must be added in groups. To add accented vowels and the letter “ñ” of Spanish, you must add the C3 page (195 in decimal) of UTF-8:

CHARACTER	BYTES
Á	c3 81
É	c3 89
Í	c3 8d
Ñ	c3 91
Ó	c3 93
Ú	c3 9a
á	c3 a1
é	c3 a9
í	c3 ad
ñ	c3 b1
ó	c3 b3
ú	c3 ba

The definition to accept identifiers in Spanish, will allow C3 page, valid as the first character and C3, 81, 89, 8D, 91, 93, 9A, A1, A9, AD, B1, B3, and BA bytes as characters below. The definition would be:

  <Identifiers CharsStart= "A..Za..z _ &#xc3;"
Content="A..Za..z0..9_&#xc3;&#X81;&#X89;&#X8D;&#X91;&#X93;&#X9a;&#XA1;&# XA9;&#XAD;&#XB1;&#XB3;&#XBA;">
  </Identifiers>

When the highlighter find the character C3, as the first character for identifiers, know that it is the beginning of a UTF-8 character and consider all C3 page as valid, causing identifiers can begin with accented vowels. The definition of these characters is not accurate, because the highlighter always treat these characters as a single byte, but work quite well for the Spanish.

A simplified form for the definition would be:

  <Identifiers CharsStart= "A..Za..z_&#xc3;" Content="A..Za..z0..9_%HIGH%">
  </Identifiers>

In this case, any UTF-8 character as a valid character for the following characters are allowed.

With these definitions, the words "ícaro", "ñandú" and "así" are recognized as identifiers.

For more information about identifiers with UTF-8, see section 5.5 - Defining identifiers.

## Special Identifiers

The special identifiers are defined in the IDENTIFIERS element:

<Identifiers>
  <Keyword>
    list of identifiers
  </Keyword>

  <Variable>
    list of identifiers
  </Variable>

  ...

</Identifiers>

Defined separately, each of these groups can be associated with a different attribute.

Reserved words are identified as "Keyword" in the syntax file:

  <Keyword>
    List of keywords
  </Keyword>
These reserved words are defined for each language. For example Pascal keywords could be defined like:

  <Keyword>
    abstract and absolute assembler begin asm array as break case class constructor const continue default destructor do downto dispose div else false end exit far forward for finalization finally Implementation in function goto if index inherited inline initialization interface mod label name is not new nil object of on operator program or procedure override private property protected public published register read record set repeat self saveregisters string then a true try to use var type unit Until With virtual while xor
</Keyword>

There is no need to put the words in a specific order. Simply put separated by spaces or line breaks.

For optimization reasons, special identifiers can only start with an English alphabetic character or any of the characters _, $,%, @ and &. If the special identifier does not start with these characters it will not be defined in the highlighter.

For example you can not add the special identifier "#uno" even though the "#" is a valid initial character for identifiers.

If the option CaseSensitive is FALSE (default), the case of the words will be ignored. Other way, the list will be reading, considering the case.

All special identifiers that are defined must also meet the rules for the definition of identifiers. For example, you can not set "$ INCLUDE" as a special identifier, if the character $ is not part of the initial characters valid for an identifier.

It is advisable not to include a large number of special identifiers, because despite being optimized search of special identifiers, you can get a deterioration in performance highlighter.

It is important that these lists special identifiers are unique, otherwise an error is generated in the load.

While the order in which the special identifiers are declared in the XML file does not affect the syntax, it can affect the performance of highlighter. For faster processing, we recommend putting words in the language that are most likely to appear first, or respecting the alphabetical order of the initial character (internally sorted by the initial character) first.

For example, if in a given language the keyword END appears more frequently than the word ECHO the list should be:

<Keyword>
    ...
end echo
    ...
</Keyword>

There is an alternative way to declare the special identifiers from outside the <IDENTIFIERS> element:

<Identifiers>
  ...

</Identifiers>

<Keyword>
  list of identifiers
</Keyword>

The highlighter automatically assumes that these definitions of special words belong to the <IDENTIFIERS> element. However this form is only valid for KEYWORD attributes.

You may require a special identifier using its horizontal position. The "TokPos" parameter specifies the position in which you must find the token to be considered as a special token.

In the following definition we require the identifier "START" to be considered as a special token only when it appears as the first token of the line.

  <Identifiers>
    <Keyword TokPos="1">
    initiation
    </Keyword>

  </Identifiers>

The difference is, now the "TokPos" parameter is used to indicate that the special identifier, must be at the beginning of the line (token number 1), to be considered as such. In any other position, in which the token is found, it will be considered as a special identifier.

Likewise it may indicate that the token occupy the 2, 3 or any other. The first token to appear in a line will always be number 1, and so on. Do not forget that even the spaces are also a token.

By default, the value of "TokPos" is zero, which means it does not consider the order to occupy the token. But in defining "TokPos", you are giving a parameter, so that may be in the highlighter, two special identifiers with the same chain but different token position. That is, the following definition will not generate error:

  <Identifiers>
    <Keyword TokPos="1">
    initiation
    </Keyword>
    <Keyword TokPos="3">
    initiation
    </Keyword>

  </Identifiers>

However, if the following definition will fail, since there is a crossing in the definitions:

  <Identifiers>
    <Keyword TokPos="1">
    initiation
    </Keyword>
    <Keyword>
    initiation
    </Keyword>

  </Identifiers>

### Special identifiers in UTF-8

TSynFacilSyn, let us to define special identifiers using UTF-8, but only the $ C3 code page UTF-8. This page includes accented characters and the letter "ñ" in Spanish, and other characters from the Latin languages.

To define a special identifier with extended characters from UTF-8, you must first be defined identifiers support UTF-8 characters (see section 4.5.1 - UTF-8).

Once they are set correctly identifiers, the definition of special identifiers is similar to that of any other special identifier, by noting that the XML format not directly recognizes UTF-8 characters.

To indicate a UTF-8 character in XML, write the UTF-8 character as two bytes with UTF-8 corresponding codes.

In the following definition defines the spanish words "ícono" and "ñandú" as keywords:

  <Identifiers CharsStart= "A..Za..z_&#xc3;" Content = "A..Za..z0..9_%HIGH%">
    <keyword>
&#xc3;&#XAD;cono &#xc3;&#Xb1;and&#xc3;&#xba;
    </keyword>
  </Identifiers>

It should be noted that although you can define special identifiers with extended characters in UTF-8, The "CaseSensitive" flag has no effect. The highlighter SynFacilSyn can not convert the text case for extended UTF-8 characters.

## Defining Tokens by content

There are several ways to define tokens by content. But all must be aware that:

• If the "Attribute" field is not specified, the new type of token created, won't be highlighted.
• We can only define up to 4 tokens by content, additional to identifiers. This limitation is imposed by criteria of speed.
• The characters to use as valid leading characters, must not conflict with the definition of other tokens of content (such as identifiers or numbers). To be the case, the last definition found is used.
• If we are going to define tokens by content, it is highly recommended also define identifiers, because if it is not defined, a default definition will be assumed, which can override the definition of the other tokens by content.
• The tokens by content will never occupy more than one line.

### Simple definition

The tokens by content, are defined rather like identifiers, but with more freedom in the start delimiter.

They are defined with the label <Token>, and using always the parameter “Content”.

It has the following valid parameters:

CharsStart	Optional	List of characters considered valid as the first character.
Start	Optional	String that is used as the starting delimiter token.
Content	Required	List of characters following characters considered valid as an identifier.
Attribute	Optional	Indicates the attribute to use for the token. If not specified, the NULL attribute is assumed.

The definition of tokens by content, can take two forms:

   <Token CharsStart=... Content= ... > </Token>

   <Token Start=... Content= ... > </Token>

The "Content" parameter is required, but the "CharsStart" and "Start", parameters can be exchanged.

We use "CharsStart" when we mean that a character (from a list) is sufficient to determine the start of a delimited token.

For example a definition of this type would be:

<Token CharsStart="0..9" Content = '0..9' Attribute='NUMBER'>
</Token>

"CharStart" indicate the list of valid characters that determine the start of a token by content.

Both, "CharsStart" and "Content", can include any printable characters, including alphabetic characters.

When you want to define tokens for content beginning with a string of more than one character should be used alternatively:

  <Token Start="0x" Content = '0..9A..Ha.h' Attribute='STRING'> </Token>

This example can be used to identify the hexadecimal numbers in C.

The "Start" parameter in this case is a delimiter token and therefore have the restrictions in section 3.5 - Token.

The tokens by content, are often used to define elements as numeric constants. A typical definition of numbers would be:

<Token CharsStart=".0..9" Content = '0..9' Attribute='NUMBER'></Token>

They are also often used to define tokens for content items that can not be handled as identifiers, because not meet that definition. For example strings in Object Pascal expressed as # 32 or # 9, can be expressed as tokens of content that begin with the # character and numeric digits followed:

<Token CharsStart="#" Content = '0..9' Attribute="STRING"></Token>

### Tokens by content and identifiers

The simplified definition of tokens by content, can lead to confusion with the definition of identifiers.

Note that the simplified form:

<Identifier CharsStart= "A..Za..z" Content = "A..Za..z0..9_"></Identifier>

It is different from the definition of identifiers:

<Identifiers CharsStart= "A..Za..z" Content = "A..Za..z0..9_"></Identifiers>

The first is a simplified form of:

<Token CharsStart= "A..Za..z" Content = "A..Za..z0..9_" Attribute='IDENTIFIER'>
</Token>

But the second is a special definition for identifiers, which are tokens of content, but that have special treatment in the highlighter.

The definition <Identifiers> indicates the highlighter we're defining identifiers highlighter. These identifiers to define subsets of tokens to assign another attribute (see Section Special Tokens) while the form <Identifier>, is only the simplified form of tokens by content with attribute IDENTIFIER, but this definition does not support to define subsets of tokens.

### Regular Expressions

The highlighter SynFacilSyn, supports the use of regular expressions (Regex) for some definitions. However, the support is basic and only some structures are recognized. These are:

ITEM TYPE	EXAMPLES	MATCHING RULE
Literal string	"x", "home", "a b", / "Hello\-world"	String (more than one character) that exactly matches the literal.
List of characters	"[0-9]", "[A-Za-z_$]"	A character that is equal to some character from the list.
Reverse List os characters.	“[^0-9]”, “[^a-zA-Z]”	A character that is not equal to any character from the list.
List of characters with quantifier "*"	"[abc]*"	String containing 0 or more characters from the list.
List of characters with quantifier "?"	"[abc]?"	String containing 0 or 1 character from the list.
List of characters with quantifier "+"	"[abc]+"	String that contains 1 or more characters from the list.
Character with quantifier	"a+"	One character string with a quantifier.

As the characters "\", "*", "+", "?", "-", may have a special meaning in the regular expression should be written as escape sequences, putting the "\" character before.

Lists of characters are shown as characters enclosed in brackets. These lists may only contain characters. Also within lists, the character "-" is used to define character ranges.
When you have an expression like "asa+", the part "a+" (character with quantifier), becomes internally, to the type list with quantifier, so the expression will be in the form "as[a]+" .

The character "-" has a special meaning inside lists, and avoids having to write over the complete range of explicitly characters. Thus the list "[a+z]" is equivalent to "[abcdefghijklmnopqrstuvwxyz]".
To use the character "-" in a list, it should be written escaped "\-". If the character "-" is at the beginning of the interval (or at the end), as in "[-0-9]", it is read as a single character.

Note that a regular expression of a character such as "a", is equivalent to a list of a single character "[a]" or "[Aa]" (If CaseSensitive = "FALSE"). In some cases it may be convenient to use the list instead of the string, to achieve better performance.

The following escape sequences have special meaning:

SECUENCIA	SIGNIFICADO
\d	It indicates a numeric character. It is equivalent to [0-9]
\D	It indicates a non numeric character. It is equivalent to [^0-9]
\a	It is equivalent to [A-Za-z]
\w	It indicates an alphanumeric character. It is equivalent to [A-Za-z0-9]
\W	It indicates an non alphanumeric character. It is equivalent to [^A-Za-z0-9]
\s	It indicates an space.
\S	It indicates an non space.
\t	The tab character
.	Any character.
\x$$	It indicates an ASCII character, where "$$" is the hexadecimal ASCII code .

### Definition using Regex

We can use regular expressions to define a token by content.
They are defined with the label <Token>, having always the "Regex" parameter.
The following parameters are accepted:

CharsStart	Optional	List of characters considered valid as the first character.
Start	Optional	String that is used as the starting delimiter token.
Regex	Required	Regular expressions to define the scope of the token.
RegexMatch	Optional	If equal to "Complete", force to compare the entire regular expression, otherwise there will be a partial detection.
Attribute	Optional	Indicates the attribute to use for the token. If not specified, the NULL attribute is assumed.

             An example of definition to extract numbers, would be:

<Token CharsStart="0..9" Regex="[0-9]*" Attribute='NUMBER'>
</Token>

            It can be used both "Start" as "CharsStart" (but not at the same time), to indicate the starting delimiter of token. Note that the syntax for specifying intervals, is different in the "CharsStart" parameter (..) and in the regular expression (-).
The "Regex" parameter contains a regular expression that will determine how the token is extracted. The regular expression must have only the elements supported by the highlighter (see previous section). For example the expression "[0-9].[0-9] *", generate an error, because it includes the point symbol, which is not supported.
The "CaseSensitive" flag, will take effect when the "Start" parameter is used, and within regular expression, in parts using string literals. For example the definition:

   <Token Start="a" Regex="[0-9]b" Attribute='Number'> </Token>

            Will coincide with "A1b" or "A1B" if it has "CaseSensitive" set to FALSE. The ranges in brackets are always case sensitive.
A more elaborate example, to recognize decimal number would be:

<Token CharsStart="0..9" Regex = '[0-9]*[\.]?[0-9]+' Attribute='NUMBER'>
</Token>

             Basically what the highlighter does is use the parameter "CharsStart" or "Start" to determine that the token has been detected and then will use the regular expression to extract the remaining characters.
The expression "Regex" is evaluated by parts. If a part matchs, it is considered part of the token, if a party does not match, it is determined that there the token ends. For example, in the following statement:

<Token CharsStart="0..9" Regex="[a-z][0-9]" Attribute='EJEMPLO'>
</Token>

            If the source string is "0a9bbb" it will be taken the token "0a9" which meets the full expression.
But if the source string is "0abbb", the token "0a" will be taken, because only at that point the match is done.
To force the text completely matches "Regex" to be considered part of the token, use the "RegexMatch" flag.
Thus, if the definition is used:

<Token CharsStart="0..9" Regex="[a-z][0-9]" RegexMatch="Complete"
       Attribute='SAMPLE'>
</Token>

            And if the source string is "0abbb" is found, only the token “0” will be taken, because only that character meets the delimiter "CharsStart". The starting delimiter, once recognized, will always be part of the token.

If you try to define a token with an invalid expression, the highlighter will generate an exception with an error message.

Unlike the simple definition, tokens with regular expressions, allowing more power to define the characters following the starting delimiter.

### Simplified definition using regular expressions

It is possible to dispense with the "Start" and "CharsStart" parameters to define a token by content, so that only the regular expression is specified:
For example, it can be easily defined numbers with decimal:

<Token regex = '[0-9][0-9]*[\.][0-9]*' Attribute='NUMBER'>
</Token>

And floating point numbers with scientific notation:

<Token regex = '[0-9][0-9]*[\.]?[0-9]*[eE][+-]?[0-9]+' Attribute='NUMBER'>
</Token>

            This simplified definition, is similar to the full definition, but considering that the first part of "Regex" is used to define the starting delimiter. For example the definition:

<Token Regex="[0-9][0-9]*" Attribute='NUMBER'>
</Token>

            It is equivalent to:

<Token CharsStart="0..9" Regex="[0-9]*" Attribute='NUMBER'>
</Token>

            As the first part of "regex" is used to define the starting delimiter, it can be deduced that the following considerations apply:

CONSIDERATION 1:
The expression "Regex" must begin with a string literal or a character list without quantifier or withthe quantifier “+”. For example, the following expressions are valid: Regex="[0-9][0-9]*" Regex="String[A-Za-z]*" Regex="\[[0-9]*" / Regex="[0-9]+" //Quantifier “+”. Equivalent to "[0-9][0-9]*" The following expressions are invalid: Regex="[0-9]*[0-9]*" <-Start with list with quantifier “*” Regex="a?[0-9]*" <-Start with character and quantifier “?”
CONSIDERATION 2:
The "CaseSensitive" parameter affects at the parts of the expression that are string literals. For example the expression: Regex = "a[0-9]b" Completely match "a0b", "A0b", "A1B" ...
CONSIDERATION 3:
String literals, when used as initial part of the regular expression are treated as delimiters. Ie they must comply with the rules defined for delimiters. For example, the following expression generates an error: Regex = "num![0-9]*" If the character "!" Is not part of the following characters in an identifier. In other words, the expression will fail if "num!" is not a valid delimiter.
CONSIDERATION 4:
The identifiers, when used as initial part of the regular expression should not be followed by expressions involving part of the identifier. For example, the following expression: Regex = "num[0-9]*" Will not work to detect the strings "num0", "num1" ... , because when it is found the string "num0", whole string will be read as an identifier and will not match the string "num", which is the starting delimiter of the regular expression.

### Advanced Definition using regular expressions

The common definition of tokens using regular expressions, or the simplified definition, can not take too much control over the extraction of tokens. Just extract to where the expression is true or extract only the delimiter.
The advanced definition, can control the flow of tokens by exploring the content so that you can control how long the text will be extracted.
As an example, a common definition would be:

<Token CharsStart="0..9" Regex = '[0-9]*\.?[0-9]* ' Attribute='NUMBER'> </Token>

Expressed in the advanced form, would be:

<Token CharsStart="0..9" Attribute='NUMBER'>
  <Regex Text="[0-9]*" ></Regex>
  <Regex Text="\.?" ></Regex>
  <Regex Text="[0-9]*" ></Regex>
 </Token>

What is done in this definition, is to separate the regular expression in simple parts (string literals or lists with or without quantifiers). The advantage is that the labels <Regex>, allow additional flow control parameters. These parameters are:

Text	Required	Text of the regex. It should be a simple expression or string literal list with or without quantifier, according to that indicated in 4.6.3 - Regular Expressions.
ifTrue	Optional	Instruction to execute in the event of coincidence with the expression indicated in "Text" is found.
ifFalse	Optional	Instruction to execute in the event of non coincidence with the expression indicated in "Text" is found.
atTrue	Optional	Attribute assigned to the token in the event of coincidence with the expression indicated in "Text" is found.
atFalse	Optional	Attribute assigned to the token in the event of non coincidence with the expression indicated in "Text" is found.

The "ifTrue" and "ifFalse" parameters are strings that include an instruction. The possible instructions are:

INSTRUCTION	DESCRIPTION
next	Jump to the next instruction
exit	End the scan and exit.
exit(n)	End the scan, and jump “n” instructions before to exit. “n” could be negative.
move(n)	Move the scan “n” instructions <Regex ...>. “n” could be negative.

These instructions allow to control the flow of the token exploration, within the highlighter. The highlighter is immune to the case, so it is the same "exit" to "EXIT".

An example of how to process integer, decimal or scientific notation numbers would be:

 <Token CharsStart="0..9" Attribute='NUMBER'>
   <Regex Text="[0-9]*" />
   <Regex Text="[\.]" IfFalse='move(+2)' />
   <Regex Text="[0-9]+" IfFalse='exit(-1)' />
   <Regex Text="[eE]" />
   <Regex Text="[+-]?" />
   <Regex Text="[0-9]+" IfFalse='exit(-2)' />
 </Token>

This definition uses jump instructions to avoid, match incomplete sequences of chars. Unlike a common definition, this definition has the advantage of not recognizing incomplete tokens, like "12." or "1.23e"

The "ifTrue" and "ifFalse" parameters, allow real control of the highlighter exploration flow, so we can create complex definitions of tokens.

The "move" instruction specifies the offset with respect to the current instruction, of the current pointer of the highlighter (lexer).

Consider the following code sequence:

  ...
  <Regex Text="[0-9a-fA-F]+" IfTrue='move(6)' IfFalse='next'></Regex>

  <!--comment-->
  <Regex Text="[^']*" ></Regex>
move(-3) :
3 instructions back.
  <Regex Text="'" IfTrue='exit'></Regex>
  <!-- comment -->
  <Regex Text="'" IfFalse='move(-3)'></Regex>
  ...

If the last statement is no coincidence, the instruction "move (-3)", will be executed, and the exploration will recede three instructions.

The target instruction is obtained by adding the offset to the current address. Then the process begins again running the new instruction that we have moved.

The "exit" instruction makes the exploration is suspended and not following instructions <RegEx> is verified. It is common behavior when Regex highlighter finds a sequence that does not match.

The parameter of "exit" (if included), allows to exit, leaving the highlighter in a different position. It is indicated as an offset, similar to what is done with the "move" instruction.

Thus, in the following code:

  ...
  <Regex Text="[0-9]*" />
  <Regex Text="[\.]" IfFalse='move(+2)' />
  <Regex Text="[0-9]+" IfFalse='exit(-1)' />
  ...

If the last instruction has no coincidence with the expression "[0-9]+", the "exit(-1)" instruction is executed, which means that the scanning will end leaving the position it was, when beginning the scan of the previous instruction:

  <Regex Text="[\.]" IfFalse='move(+2)' />

This instruction will not be evaluated before leaving, simply it will used to obtain the position that the highlight had, when it began to evaluate this statement, or put in another way, when it finished exploring the above instruction. This shows that the highlight saves the scanning position of the text, for each instruction is executed.

When "ifTrue" and "ifFalse" parameters are not specified, the default values are the instructions "next" and "exit" are assumed. Which means that the exploration will go until to find an expression that does not match.

A further advantage of this form of definition is that you can decide "on the fly" the attribute type that the token will have, according to its content. It is, unlike any other definition in the highlighter, the initial character, not necessarily define the type of final attribute.
To change the attribute, the "atTrue" parameters and "atFalse" will be used. Consider the following example:

  <Token CharsStart="'" Attribute='STRING'>
    <Regex Text="[^']*" ></Regex>
    <Regex Text="'" ></Regex>
    <Regex Text='b' IfTrue='exit' atTrue='NUMBER' IfFalse='next'></Regex>
  </Token>

With this definition, the tokens that are in single quotation marks are recognized as strings, but if the character "b" after the chain was found is assumed to be a number.

The values ​​specified in the "atTrue" and "atFalse" overlap the specified parameters in the <Token ...> attribute.

The final attribute acquired by the current token, is the last that has been assigned to "atTrue" or "atFalse" (or defined in the <Token ...>), upon completion of the scan, either because an instruction is executed "exit" or finished executing all instructions.

In fact, although not specified, these parameters are always read, but their default values ​​are the same attribute specified in the <Token ...>

There is no practical limit to the number of instructions <Regex ...> that can be used in a definition, but logically, many instructions make exploration highlighter becomes slow.

For information on the instructions that are supported, see Section 5.5.2 - Advanced Settings

## Definition of delimited Tokens

Delimited tokens are another way to define tokens alternately to the definition of tokens for content.

Are defined with the label <Token>, having always present the parameter “End”.

Attributes include:

Start	Mandatory	Initial delimiter token. It can be a symbol or identifier.
CharsStart	Optional	List of valid characters to be at the beginning.
End	Optional	Delimiter end of the token. It can be a symbol or identifier.
Attribute	Optional	Indicates the attribute to use for the token. If not specified, the NULL attribute is assumed.
Multiline	Optional	Indicates whether the token can span several lines or if a single line. The default is a single line.
Folding	Optional	Indicates whether the fold mark is displayed in the editor. Only valid for multiline tokens. By default, it is disabled.
Escape	Optional	Specifies an escape character, which is used to skip the next character of the exploration.

A typical delimited token, here is the definition of strings:

<Token Start="'" End="'" Attribute='STRING'></Token>

This statement assigns the STRING attribute to the string that is between single quotes, including quotes.

If we want the strings can be extended for more than one line and also can fold, the following code will work:

<Token Start="'" End="'" Attribute="STRING" Multiline="True" Folding="True">
</Token>

A text with this highlighter, could be shown as follows:

The following example defines the Pascal compiler directives:

<Token Start="{$" End="}" attribute="DIRECTIVE"></Token>

This definition would identify blocks of type:

{$I+}

Here is another example defining directives used in C:

<Token Start="#" End="&gt;" attribute="DIRECTIVE">
</Token>

This definition would identify blocks of type:

#include <windows.h>

If the final delimiter of a delimited token is not specified, or is assigned the empty string, is assumed to extend to the end of the current line. This behavior is common in defining single-line comments:

<Token Start="//" attribute="COMMENT"></Token>

The "CharsStart" parameter allows us to specify a list of characters as initial delimiters for a limited token (similar to how it's made in tokens by content), but it is not usual to use this form of definition.

The attributes that can be assigned are all handled the highlighter:

1. EOL
2. SYMBOL
3. SPACE
4. IDENTIFIER
5. NUMBER
6. KEYWORD
7. STRING
8. COMMENT

You can define as many delimited tokens as you want, considering that the more of them, the greater the processing speed will be for the highlighter.

For a token delimiters are generally symbol type, but may also be of type identifier (see Section 3.5 - Token Delimiters).

Strings and comments are classic examples of delimited tokens.

## Escape character

In certain string syntax definition, can include the delimiter as part of the same chain, using an escape character. For example, in different languages, strings allow you to include the double quote character or single quote within the same string, if they are written with the "\":

  MyString = "character \" is the double quotation mark. ";

To define string tokens to recognizing these escape sequences, without dividing the string, you must specify "\" escape character. The following definition of a delimited token performs this functionality:

  <Token CharsStart='"' End='"' Attribute='STRING' Escape="\">
  </Token>

The following conditions must be met for the definition of a escape character:

1. The escape character can be specified only in fefinition of delimited tokens.
2. Only one escape character can be defined for each definition of delimited token.
3. The escape character must be exactly one character width.
The escape character can only be specified in definitions where the starting and ending delimiter are of a character width, and equals (as in the definition of strings).
## Defining strings

Strings are common delimited tokens. The delimiters are usually the quote and double quote, but depends on the language used.

To define the strings can use the simplified definition of tokens:

<String Start="&quot;" End="&quot;"></String>

If we do not specify if the strings are of multiple lines, they are assumed to be single-line strings. To define multi-line strings must be specified:

<String Start="&quot;" End="&quot;" MultiLine=”True”>
</String>

## Defining comments

Comments are also common delimited tokens, like strings. Can be a line or multiple lines:

If the ending delimiter is not specified, it is assumed that it is the newline, ie it is a comment line.

For example, to define a single line comments with the # character, would:

<Comment Start="#" ></Comment >

To define multi-line comments must specify the ending delimiter and the "Multiline" attribute:

<Comment Start="/*" End="*/" Multiline="True"></Comment >

If the definition of comments is not specified, no definitions are created by default, or in other words, no comments were recognized.

The comment delimiters can not be the delimiters instead of strings.

## Block Definition

The blocks are defined with the labels <Block> and </ Block>.

Has the following parameters:

Start	Optional	Initial boundary of the block. Must be an identifier or special symbol.
End	Optional	Delimiter end of the block. Must be an identifier or special symbol.
Name	Optional	It is a string that identifies the block within the file syntax. It is the name of the block. It must be unique for each block.
Folding	Optional	Indicates whether the fold mark is displayed in the editor. This mark appears only when the block has more than one line. By default, it is enabled.
Parent	Optional	Indicates the parent of the block. The default is "NONE", ie it is not restricted to any block.
BackCol	Optional	Indicates the background color to be painted, all tokens that are within the block.
CloseParent	Optional	Indicates when closing the block, it must be closed the parent block too.

The "Start" and "End" parameters should be actually mandatory, but are considered optional because you can set later using an alternative definition (see Section 4.11 - Advanced Blocks).

A particular detail, is that there is not the attribute parameter, because the blocks have not visible attributes. The "BackCol" parameter allows color the background of tokens belonging to a block, but this color will only take effect when the ColorBlock = "Block" option is enabled in the language definition.

A typical case is the block used in Pascal:

  <Block Start="Begin" End="End" >
  </Block>

This block will extend from after the token "BEGIN" to the end of the token "END". The block may be distributed in one or more lines. Is not necessary to specify. The blocks are multiline by default.

The "Name" property lets us to specify a name for the block. If we do not specify a name, the highlighter, will assign an internal name, which has the form "blk1", "Blk2" ... depending on how many blocks there are.

We can assign any name to a block, except "Main", "MultiToken" and "None", which are names reserved for internal work highlighter.

The name itself is not important for the work of the block, but it is useful for when you want to reference it from another part of the syntax file.

The following case is an example of block name:

  <Block Name="Begin-End-Global" Start="Begin" End="End" ></Block>

The name assigned to the block must be unique, otherwise an error is generated when reading the syntax file.

The main use of a block is for code folding. By default, a block will always display the code folding mark (unless it is contained on one line). But if we want to formally specify it, we should do:

  <Block Start="Begin" End="End" Folding="True"></Block>

If we want a defined block, but not fold mark, we should specify this parameter Folding = "False".

A text with fold mark in a block would look like:

Block delimiters can also be symbols. For example, the following statement is valid:

  <Block Start="{" End="}">
  </Block>

This definition, consider all tokens within the braces as part of a block, as is done in C.

Block delimiters must always be identifiers or special symbols. If a delimiter block that is not defined as a special token is defined, it is created first as a special token before processing the block.

For example, in the following definition:

  <Block Start="Start" End="End" Folding="True"></Block>

If the identifier "Start" was not created as a special identifier, then first "Start" will be created as a special token, within the highlighter, with the "tkIdentif" attribute.

If the special identifier already existed, it is not created again nor its attribute is changed.

In creating blocks, the uniqueness of the delimiters are not validated. For example, you can write this definition, without generating errors:

  <Block Start="Begin" End= "End"> </Block>
  <Block Start="Begin" End= "End"> </Block>

Although we use the same delimiter, actually we would be creating two separate blocks, but would generate confusion because the same delimiter is the start of two blocks, so that when the highlighter find the delimiter "Begin" opens only one.

When blocks with the same Start and End delimiter are defined, you should always restrict a parent block, because otherwise not be able to close the block. Consider the following definition:

  <Block Start="'" End ="'" Name="Blk_comill"> </Block>

As defined, this block is never closed, because each new occurrence of the quote, be understood as the beginning of another nested block. To achieve that end could restrict its validity to the main block.

  <Block Start="'" End ="'" Name="Blk_comill" Parent="Main"> </Block>

We conclude that a block of this type (same starting and ending delimiter), can never be nested.

### Colored blocks

The blocks are mostly used for the implementation of code folding. But, these blocks generally correspond also to syntactic structures of the language of the text.

As an additional feature, the highlighter color the background allows the blocks to provide a visual aid, the extension block., In addition, only show fold marks extension block level rather column lines .

To activate the colored blocks, you should set the language to "ColorBlock" parameter to "Level" or "Block".

When we set ColorBlock in "Level", will proceed to do an automatic blocks coloring, using the nesting level of each block. The following example shows how a simple C code would look with colored Level:

In this style of colored, the innermost block appear with both darker purple hue, both have nesting level block. The base color is not configurable per file or instructions, but can be changed by changing the unit of highlighter.

The other colored is colored by block. ColorBlock If the parameter is set to "Block" will be colored using as background color, the color defined for each block. The figure below shows how the same text would be using colored blocks.

This type of colored, does not take into account the level of nesting, but uses the custom color that is specified in the definition of each block.

To create this effect, we have used the following definition:

<?Xml version="1.0"?>
<Language name="C" ext="C" ColorBlock="Block">
  <Block Name="Int" Start="Int" End=")" Parent="Main" Backcol="#81F7F3">
  </Block>
  <Block Name="Bloque_de_C" Start="{" End="}" Parent="Main" Backcol="#F3F781">
    <Block Start="{" End="}" Backcol="#F5DA81"> </Block>
  </Block>
</Language>

Color, defined for each block specified in "BackCol" parameter. This color should always be specified in "#RRGGBB" format. Where RR, GG and BB correspond to the values ​​of the Red, Green and Blue components, expressed as two hexadecimal digits.

If you want the block does not define a color, but the color of the previous block is displayed, you can use the transparent color:

<Block Name="Parameters" Start="(" End=")" Folding="False"
       Backcol="Transparent"> </Block>

It should be noted that by using the colored block work requires more processing in the highlighter, which when used for level highlighted.

### Scope of a block

So far, we have defined blocks that are valid anywhere in the code. For example when we define:

  <Block Name="C_block" Start="{" End="}">
  </Block>

We are saying that we want all tokens that are in braces, are part of the block "C_block".

So if we write C code with this syntax, we get the following image:

The highlighter is activated colored blocks per level.

In the picture you can clearly see that the two blocks have been recognized in the syntax. One of them is a nested block, but still valid. We could create countless nested blocks this way.

This is because in the block definition, have not specified the scope of the block in the "Parent" parameter. So is assumed to be the "None", ie it is valid block anywhere where it appears.

The same result would have obtained had we explicitly since the block is valid anywhere using the following form:

  <Block Name="C_block" Start="{" End="}" Parent="None"></Block>

The block "None", is actually a reference to any block. It is not an actual physical block. No properties.

There are 3 predefined highlighter blocks:

"None" -> Refers to any block.
"Main" -> Identifies the main block. He who has no nesting.
"MultiToken" -> refers to the building blocks of all tokens that have enabled multi folding.

You can limit the validity of a block specific areas of code that can be blocks or sections.

To explicitly define a block is valid only within the confines of another block, we must indicate the name of the block. For example, the following definition creates first block "AQUI_SI ... END", and then define the block "{}", for that is only valid within this block:

  <Block Name="Aqui_si" Start="AQUI_SI" End="End"></Block>
  <Block Name="Bloque_de_C" Start="{" End="}" Parent="Aqui_si"></Block>

A sample code will show the effect of this definition:

As shown, the second block is not recognized because it is outside of the block "Aqui_si".

Be careful, to restrict a range block. Especially nested blocks can appear. For example if we define the block "{}", To only be valid in the main block:

  <Block Name="C_block" Start="{" End="}" Parent="Main"></Block>

We could have the following result:

And we note that the second key "{", found not open another block, because it is not within the main block. However the first key "}" found, recognizes itself as the final delimiter of the block, excluding some of the code and giving rise to an erroneous definition syntactically.

The block "Main" is the one that includes the entire file. All tokens and blocks (or sections), believed to be directly or indirectly contained in the block "Main".

It is not necessary, create the block "Main", this block always exists and is unique. If we had defined his statement would be something like this:

  <Block Name="Main" Start="" End="" Parent=""></Block>

The interior of any block, is no longer part of the block "Main". Only tokens or structures that are not within another block, pertain directly to the block "Main":

It belongs to the block "Main"
No belongs to the block "Main"

When blocks are only valid in the block "Main", they are preventing these can be nested and may appear only in the main body are created.

You can limit the nesting level of a block. This requires specifying the structure, each block corresponding to each level.

The following example is a definition to allow nesting of one second block "{}":

  <Block Name="C_block" Start="{" End="}" Parent="Main">
  </Block>
  <Block Start="{" End="}" Parent="C_block" >
  </Block>

Now with this definition, be permitted to include a block "{}", within another, but no more. So if a third nesting inclusion, the syntax will fail:

As we have seen, the "Parent" parameter defines hierarchy of blocks a tree way. But as an improved definition syntax, we can use nested definitions, to indicate this hierarchy, without using the "Parent" parameter.

For example, the following definition:

  <Block Name="Aqui_si" Start="AQUI_SI" End="End">
  </Block>
  <Block Name="C_block" Start="{" End="}" Parent="Aqui_si">
  </Block>

It can be written in simplified form as follows:

  <Block Name="Aqui_si" Start="AQUI_SI" End="End">
    <Block Name="C_block" Start="{" End="}"> </Block>
  </Block>

This form avoids using the "Parent" parameter and is clearer. Therefore it is the preferable way to be used.

### Closing the Parent block

The "CloseParent" parameter allows to force the closure of the parent block, when a child block is closed.

This is a way to close two blocks simultaneously, using the same closing delimiter. As an example, consider the following Pascal code:

This structure contains two blocks: "procedure ... end" and "begin ... end", starting in different positions, but nevertheless, must end with the same delimiter "end".
A simple definition like this:

 <Block Start="Procedure" End="End">
   <Section Start="Var"> </Section>
   <Block Start="Begin" End="End"></Block>
 </Block>

Will not work properly for this syntax, because the delimiter "end" will be recognized only for the block "begin ... end" leaving without closing the block "procedure ... end".
To successfully implement this folding structure, we must use this definition:

 <Block Start="Procedure" End="End">
   <Section Start="Var"> </Section>
   <Block Start="Begin" End="End" CloseParent="true"></Block>
 </Block>

The use of "CloseParent" parameter will do when closing the block "begin ... end", the block "procedure ... end" will be also closed.

### Order matters

There may be situations where there are two block definitions apply to the same case. Consider we want to implement the recognition of a Pascal code, including declaration of procedures, as shown in the following figure:.

The XML definition (including color for blocks like help) could be:

 <Block Start="begin" End="End" BackCol="yellow"></Block>

 <Block Start="Procedure" End="End">
   <Section Start="Var"> </Section>
   <Block Start="Begin" End="End" CloseParent="true" BackCol="aqua"></Block>
 </Block>

This definition is pretty accurate, but it has two definitions for the block "begin ... end":
1. which it is valid within the body of a procedure.
2. is valid in any block, including inside procedures.
When the token "begin" within the scanning, is found, the key question is: Which of the two definitions do apply?
For getting the answer, we should know that the highlighter, not scan blocks for each token found, but when it encounters a token who is delimiter for one or more blocks, just then explores the list of blocks to find which applied.
So when it find the token "begin" within a procedure, it will begin to explore the blocks, in the order they were declared, which applies. Seen this way, the order of declaration matters.
Therefore, the answer to the question would be: "The one that is valid in any block" because it is the first to be declared. This of course will produce the wrong result, as shown in the following figure:

To get the desired effect, we must first declare the block "begin ... end" of the procedure:

  <Block Start="Procedure" End="End">
    <Section Start="Var"> </Section>
    <Block Start="Begin" End="End" CloseParent="true" BackCol="aqua"></Block>
  </Block>
  <Block Start="begin" End="End" BackCol="yellow"></Block>

The result must be like in the following figure:

Note that this definition of procedure, is defined as valid in any block, including the block of the same procedure, so that is a recursive definition. That is, they allow us to define procedures within another procedure, as shown in Figure:

## Advanced Blocks

The blocks definition, using the "Start" and "End" parameters, is a simple but limited way to specify blocks.

There is an alternative way that allows us greater freedom. This is to indicate the delimiters in nested tags <Start> and <End>.

To appreciate the difference, consider the following statement:

  <Block Start="Repeat" End= "Until" > </Block>

And alternatively, equivalent:

  <Block>
    <Start> Repeat </Start>
    <End> Until </End>
  </Block>

This way of defining blocks gives us more freedom to:

- Including the additional parameter "TokPos" in the delimiters.
- To include multiple delimiters.

The "TokPos" parameter specifies more detail regarding the delimiters. It allows us to fully identify a special token that has been declared by this parameter (See Section 4.5.2 and 4.4.1).

For example, using a definition like this:

  <Block>
    <Start TokPos="2"> Initiation </Start>
    <End> End </End>
  </Block>

Hopes to use as a starting delimiter, a special identifier that is declared as follows:

  <Identifiers>
    <Keyword TokPos="2"> Initiation </Keyword>

  </Identifiers>

If there this definition, proceed to create it, because the block delimiters required whenever there first as special tokens.

The alternative delimiters, definition allows us also define more than one start or end delimiter, for the same block.

For example if we want the BEGIN ... END block can also be open with the keyword START, then the statement would be:

  <Block>
    <Start> Begin </Start>
    <Start> Initiation </Start>
    <End> End </End>
  </Block>

Each <Start>, which is placed inside the block definition, will define one (and only one) additional initial delimiter.

Note that the spaces before and after the <Start> </ Start> are ignored. That is, it can not be included as part of the bounding areas.

Likewise, to add more delimiters end, we must use the <End>, within the block definition:

  <Block>
    <Start> Begin </Start>
    <Start> Initiation </Start>
    <End> End </End>
    <End> Finalization </End>
  </Block>

Additional delimiters will also support the "TokPos" parameter. The following example shows the definition of a block with two delimiters:

  <Block Name="Oracle_query" Start="Select">
    <End> End </End>
    <End TokPos="1"> / </End>
  </Block>

This definition uses the symbol "/" as the end delimiter and also specifies the "TokPos" parameter to specify a specific position of the token.

## Defining Sections

The sections are defined with the tag <Section>.

They support the following attributes:

Start	Optional	Initial boundary of the section. Must be a special token.
Name	Optional	It is a string that identifies the block within the file syntax. It is the name of the section. It must be unique for each section.
Folding	Optional	Indicates whether the fold mark is displayed in the editor. This mark appears only when the section has more than one line. By default, it is enabled.
Parent	Optional	Indicates the parent of the block. The default is "NONE" (unless the definition is nested), ie it is not restricted to any block.
Backcol	Optional	Indicates the background color to be painted, all tokens that are within the section. By default it is set to "None"
Unique	Optional	Indicates that only a section of this type is allowed at block containing it. Default is off.
FirstSec	Optional	Indicates that the section is opened when the block opens.

Section parameters are similar to the parameters of a block except that there is no ending delimiter, because the sections have another mechanism to determine an end.

As the sections are in fact also blocks most blocks rules apply also for sections. Coloring sections also is similar to the colored blocks.

In the following example we declare the INTERFACE section of the Pascal language:

  <Section Start="Interface">
  </Section>

This section will start after the token "interface" and continues to the end of the program if no other section is defined.

If we define two sections, we are dividing the code into two or more parts:

  <Section Start="Interface"> </Section>
  <Section Start="Implementation"> </Section>

Now we have an "interface" section may result in the initiation of an "implementation" section, if there is one.

The following figure shows a sample code with the created sections:

The order in which the sections are defined is not important. It doesn't implies some order in recognizing the sections.

We could have the following example code:

Where we can see that the sections, have been correctly recognized, and including a duplicate section.

To avoid such a section, it is recognized two or more consecutive times, use the "Unique" parameter. If activated, it will not allow a repeat section after herself. This means that only recognize the first time it appears.

To illustrate the effect of "Unique", say the same old text, but with definition Unique = "true" and the syntax. The effect would be this:

As we can see, there is only one "implementation" section (see fold mark), since the latter is not regarded as a new section. However, if it is possible to define "implementation" section again after an "interface" section as far as the highlighter is concerned.

The "Name" of a section, lets us to specify a unique name for the section. If we do not specify a name, the highlighter will assign an internal name, which has the form "Sec1", "Sec2", ..., depending on how many sections there are defined.

You can assign any name to a section except "Main", "MultiToken" and "None", which are names reserved for internal work highlighter.

The name itself is not important to the work of the section, but it is useful for when you want to reference it from another part of the syntax file.

The name of a section should be different from another section or another block.

The following case is an example of a section named:

  <Section Name="Interface" Start="Interface"></Section>

The sections also show the fold mark code by default and can be disabled with the "Folding" parameter.

The sections are often used to represent special code blocks in a programming language, such as sections "interface" and "implementation" Pascal. These language structures are not well suited to manage them as blocks.

The combination, block-section, can represent common structures in programming languages. Consider for example, the definition of Pascal procedures;

At first glance it might seem that can be expressed as nested blocks, but a more detailed analysis will reveal that there is no nesting, because part of the declaration of variables, ends when the procedure body (or any type declaration or constant begins or more variables), which in turn is nested within the procedure declaration because it uses the same delimiter.

The best way to express this structure is driving sections within a block that starts with the reserved word "procedure" and end with "end":

  <Block Name="Proc" Start="Procedure" End="End" Parent="Main">
    <Section Start="Var"> </Section>
    <Section Start="Begin"> </Section>
  </Block>

The declaration of variables, handles like a section of the block "Proc".

This definition can be completed by adding sections to the declaration of types and constants; and will work well at least for simple cases. The following example shows how a simple pascal procedure would look, using this definition:

To improve the definition, we should consider that the keyword "VAR" can also appear as a parameter switch (to indicate parameters by reference), and not to be confused with variable declaration.

To avoid this misinterpretation, you can create an additional block, including the declaration of parameters of the procedure:

  <Block Name="Proc" Start="Procedure" End="End" Parent="Main">
    <Block Name="ProcParam" Start="(" End=")" Folding="False"> </Block>
    <Section Start="Var"> </Section>
    <Section Start="Begin" Unique="True"> </Section>
  </Block>

Now with this protection, the word VAR is ignored when you it is in parentheses in the block procedure.

A further detail which is included in the above definition, is that it has become the "Unique" to TRUE parameter in the "begin" section. This will prevent every word "Begin" is recognized as the beginning of another section "Begin". Otherwise not could nested BEGIN ... END blocks within the procedure body.

## First Section

Sections usually begin after the block containing it, has begun. However, it may be that we need to open a section while a block is open.

This is what is called the "First Section".

To indicate that a section opens with the block, we use the "FirstSec" parameter in the declaration section. The following example shows how to structure an SQL query in a single block with two sections:

  <Start Block="SELECT" End=";" Parent="Main" Folding="False">
<Section Start="SELECT" FirstSec="True"> </Section>
<Section Start="FROM"> </Section>
  </Block>

As the SELECT section is declared with FirstSec = "TRUE" then this section will open just block that starts with SELECT open.

If we had just done:

  <Start Block="SELECT" End=";" Parent="Main" Folding="False">
<Section Start="SELECT"> </Section>
<Section Start="FROM"> </Section>
  </Block>

The section starts with SELECT, not open at the beginning because SELECT, is also the starting delimiter of the block and the verification of sections, is made after recognizing the word SELECT.

Visually would have the following picture:

Now we have two collapsible sections within a block, which is not folded (and who would not be accessible with mouse, if it was folding).

Sections, like the blocks also support the alternative definition for delimiters. For example, the following code shows how to create a section with two initial delimiters:

  <Section Name="Section_start">
    <Start> Begin </Start>
    <Start TokPos="1"> Initiation </Start>
  </Section>

## Blocks and sections

As defined by sections, they end when another section, of the same level starts, or when another block of the same level starts. This means that the sections can be closed with a block.

Consider the following definition:

 <Section Start="var"> </Section>
 <Block Start="begin" End="End"></Block>

Here a block is defined along with a section on the same level, so if the block appears, it will close the section. Otherwise, the section would extend until the end of the whole text (Block "Main").

The following figure illustrates this effect:

# Configuring the syntax using code

So as we can configure syntax, using an external file, it can also be done using some methods of the highlighter.

When the highlighter is created, not start from scratch. Some settings are predefined. These are:

- Predefined Highlighter attributes are created.
- The definition of tokens “end of line” is created and can not change.
- The definition of tokens “spaces” is created and can not change.
- Tokens defining symbol is created using all remaining characters.
- The definition of default identifiers are configured.
- Blocks "MainBlk" and "MulTokBlk" are created.

No strings, no comments, no keywords are configured. These must be user-defined.

The attributes automatically created in highlighter, have some properties assigned by default. For example keywords are shown with green text.

A typical sequence for using the highlighter will look like this:

you use
  ..., SynFacilHighlighter; //includes unit

procedure TForm1.FormCreate(Sender: TObject);
var
  hlt : TSynFacilSyn; //reference to highlighter
begin
  hlt : = TSynFacilSyn.Create(self); //creates highlighter
  SynEdit1.Highlighter : = hlt; //configures the highlighter
  //set attributes of tokens
  hlt.KeywordAttri.Foreground: =clGreen;
  hlt.CommentAttri.Foreground: =clGray;
  ...
  //set syntax highlighter
  ...
end;

We only need to configure the necessary attributes. The rest can be left at their default values.

Set the syntax of the highlighter, means defining lexical and syntactic rules that apply for the colored text. Can be divided essentially into two parts: The definition of tokens and block definition.

To create a new syntax, you must follow a strict sequence:

1. Clean identifier tables and special symbols: ClearSpecials()
2. Clean the method table: ClearMethodTables()
3. Defining Identifiers: DefTokIdentif()
4. Definition of numbers and other Tokens for content.
5. Definition of special identifiers: AddIdentSpec()
6. Definition of special symbols: AddSymbSpec()
7. Definition of delimited tokens (strings, comments, etc.)
8. Definition of blocks and sections.
9. Rebuilding the syntax: Rebuild()

ClearSpecials() clears the tables of special identifiers and table of special symbols. Therefore, it also deletes the definition of delimited tokens and tokens by content, that are using special tokens.

CreateAttributes() removes all attributes created (types of tokens) and creates the default attributes. This ensures that only leave predefined attributes, deleting any additional attributes that may have created later.

ClearMethodTables(), clean the method table highlighter[5]. This task is necessay because when defining the syntax, new entries are created in this table.
[5] The method table is an internal structure of highlighter used for quick recognition of tokens. It consists of an array of characters in each cell indicates a processing function of the corresponding character, so you can quickly jump to the processing function without making comparisons.

The first step in defining a syntax is the definition of identifiers, because these tokens are the basis of most languages.

The method table is an internal structure of the highlighter that allows to select, which method must process a character when scanning text is performed. The objective of using a table of methods is to accelerate the speed of the highlighter.

Clean the method table is important, whether to define identifiers or other tokens by content, because the highlighter applied, when created, a default definition for identifiers. If a new definition are specified WITHOUT cleaning the method table, both definitions would overlap.

When cleaning the method table, the definition of all tokens by content (including identifiers) and delimited tokens are cleared, so it is the first step in defining any syntax.

The first time a new syntax is created, it is not necessary to clean the tables of special identifiers, because no special identifier is created (like KEYWORDS) by default.

If only you want to add special identifiers, simply run AddKeyword()

The Rebuild() method process all special symbols and delimited tokens with initial delimiter of symbol type. If it does not run, will have no effect the indicated definitions.

## Regular Expressions

Within the definition of the syntax by code, usage of regular expressions is done. However, the highlight only supports some simple constructions such as "[az] *" or "[0-9] [.\]"

For supported constructions, go to the section 4.6.3 - Regular Expressions.
## Error Handling

Syntax configuration instructions can generate internal errors. When an error is detected in the definition of syntax or otherwise, an exception of type "ESynFacilSyn" is generated..

Therefore, it is advisable to enclose the syntax definition section in a TRY ... EXCEPT block, especially in the critical parts:

  ...
  try
    hlt.ClearSpecials;
    hlt.CreateAttributes;
    hlt.ClearMethodTables;
    hlt.DefTokIdentif('[A-Za-z]','[A-Za-z0-9]*');
    hlt.AddKeyword('BEGIN');
    ...

  except
    on e:Exception do begin
      ShowMessage(e.Message);
    end;
  end;
  ...

The highlighter can generate several exceptions, when the definition of syntax, in order to ensure that the syntax definition is consistent, and no error will be generated when the highlighter is runnig. The highlighter will run quickly, avoiding unnecessary checks.

## Token types and attributes

As already mentioned (Section 9 - Syntax elements), There are a number of types of tokens that are always created with the highlighter. These types are:

- tkEol
- tkSpace
- tkSymbol
- tkIdentif
- tkNumber
- tkKeyword
- tkString
- tkComment

The tkEol and tkSpace types have fixed definitions and can not be changed (however, the spaces can be configured in his appareance). The other types are provided, but their definitions can be adjusted with more or less freedom.

When creating an instance of the highlighter, it does not start empty. It has some previous definitions that allow you to start working. These definitions imply being able to recognize spaces, line breaks and symbols. In addition, a default definition is created for identifiers. The following diagram shows the initial state of the highlighter when it starts:

Symbol

Identifier

Line End

Space

The definitions of spaces and line breaks are fixed, ie they can not be changed. All other text is considered Symbols, but when the identifiers are created, some characters that were considered as symbols, are taken.

It is possible to remove the definition of identifiers (but not spaces, line breaks, and symbols), and this is usually done when calling ClearMethodTables. That is, after a call to ClearMethodTables, our highlighter will have the following definition:

Symbol

Line End

Space

In this case, all tokens other than line breaks or spaces are considered to be of the tnSymbol type. For more information on defining attributes see section 6.4.

## Configuring the attributes

If we want to configure the look of tokens "tnString" (which usually represent the constant strings), we should use the object “tkString”:

  hlt : = TSynFacilSyn.Create(self); //creates the highlighter
  ...
  hlt.tkString.Foreground: =clPurple; //text color
  hlt.tkString.Style : = [FsBold, fsUnderline]; //bold and underlined
  ...

We may also use an additional variable to access the attributes:

var
  atribString: TSynHighlighterAttributes;
  ...
  hlt : = TSynFacilSyn.Create(self); //creates the highlighter
  ...
  atribString : = hlt.tkString; //reference to the attribute
  atribString.Foreground: =clPurple; //text color
  atribString.Style : = [FsBold, fsUnderline]; //bold and underlined

To create new attributes, use variables of type "TSynHighlighterAttributes" similarly. In the following code we create two new types of tokens, and define its attributes:

var
  tkOperator: TsynHighlighterAttributes; //Attribute
  tnOperator: integer; //Id
  tkDelimiter: TsynHighlighterAttributes; //Attribute
  tnDelimiter: integer; //Id
...
  //creates new type of token called "operator"
  tnOperator : = hlt.NewTokType('Operator', tkOperator);
  tkOperator.Foreground: =clRed; //text color

  //creates new type of token called "delimiter"
  tnDelimiter : = hlt.NewTokType('Delimiter', tkDelimiter);
  tkDelimiter.Foreground: =clRed; //text color

Note that NewTokType returns both the token ID and the associated Attribute. The ID will be used later when the highlighter is set up.

New attributes can now be used as if they were equal to the pre-defined attributes highlighter. The name indicated in NewTokType(), is not important for purposes of configuration by code, but is useful when a program accesses the attributes of highlighter, a configuration window. This name is also used to identify the new type within the XML file.

The new type name must be unique for each type. Otherwise an exception is generated at runtime.

If you want to reference an existing attribute, by name, use the GetAttribByName() function:

  tkOperador : = hlt.GetAttribByName('Operator'); //must have been created

This way you can also access the attributes that have been created from the XML file because it is the only way to identify them externally. GetAttribByName() does not distinguish between uppercase or lowercase.

The attributes dynamically created, are added to the list of predefined attributes highlighter. To clear the list of attributes, call the method CreateAttributes(), which leaves only the predefined attributes.

To get the ID of an attribute by its name, the GetAttribIDByName function must be used:

  tnOperator := hlt.GetAttribIDByName('Operator'); //must have been created

We can also use the Attrib [] array, to get the attribute from the ID:

  tkOperador := hlt. Attrib[tnOperator];

The array Attribute[], must not be used.

## Defining identifiers

The first definition of token that we must do, within a highlighter, is for identifiers.

To define identifiers by code, you must define the initial and subsequent characters, in the form of regular expressions:

  hlt.ClearMethodTables;
  ...
  hlt.DefTokIdentif('[A-Za-z]','[A-Za-z0-9]*');

In this example assumes that "hlt" is the highlighter. The "ClearMethodTables" instruction is necessary to clean the method table highlighter.

The DefTokIdentif() method to define identifiers tokens. These are always defined by content.

The first parameter defines the valid as the first character for identifiers characters. The second parameter defines the following characters.

The first parameter is written always bracketed to indicate that this is a list of characters and not a common string. If it is not written as a list, an exception will be raised.

The second parameter defines the following list of characters that are valid for the identifier. You should always have a list: '[ ]*', otherwise an exception will be generated.

Initial and Subsequent characters can be any character, printable or not.

At the highlighter created at the beginning, it also creates a default definition for identifiers. This definition is:

  hlt.DefTokIdentif('[A-Za-z$_]','[A-Za-z0-9_]*');

This means that although not specified any definition, it always starts with one, for identifiers.

After defining identifiers, all tokens belonging to that category will become like "tnIdentif", and displayed the attributes of this type.

### Identifiers UTF-8

SynFacilSyn (from version 0.9), has a basic support for identifiers with UTF-8 characters. This way you can define identifiers with characters from other languages ​​besides English.

You can include initial characters of UTF-8 type, but the whole entire UTF-8 page of 128 characters are included. The highlighter can not filter by UTF-8 character individual (because the filter is done only by the first byte and UTF-8 characters are two or more bytes).

So for example to enable the recognition of identifiers that can begin with vowels branded Spanish, must include the following definition:

  hlt.DefTokIdentif('[A-Za-z'#195']','[A-Za-z0-9]*');

The highlighter recognize the code #195, as the beginning of a UTF-8 character, and authorize as valid initial character of an identifier to all characters of the code page 195 ($C3). This page contains all accented characters of the Latin languages: áàäéèë ... both lowercase and uppercase.

Page 195, includes the following characters:

CHARACTER	BYTES	DESCRIPTION
À	c3 80	LATIN CAPITAL LETTER A WITH GRAVE
Á	c3 81	LATIN CAPITAL LETTER A WITH ACUTE
Â	c3 82	LATIN CAPITAL LETTER A WITH circumflex
Ã	c3 83	LATIN CAPITAL LETTER A WITH TILDE
Ä	c3 84	LATIN CAPITAL LETTER A WITH diaeresis
Å	c3 85	LATIN CAPITAL LETTER A WITH RING ABOVE
Æ	c3 86	LATIN CAPITAL LETTER AE
Ç	c3 87	LATIN CAPITAL LETTER C WITH CEDILLA
È	c3 88	LATIN CAPITAL LETTER E WITH GRAVE
É	c3 89	LATIN CAPITAL LETTER E WITH ACUTE
Ê	c3 8a	LATIN CAPITAL LETTER E WITH circumflex
Ë	c3 8b	LATIN CAPITAL LETTER E WITH diaeresis
Ì	c3 8c	LATIN CAPITAL LETTER I WITH GRAVE
Í	c3 8d	LATIN CAPITAL LETTER I WITH ACUTE
Î	c3 8e	LATIN CAPITAL LETTER I WITH circumflex
Ï	c3 8f	LATIN CAPITAL LETTER I WITH diaeresis
Ð	c3 90	LATIN CAPITAL LETTER ETH
Ñ	c3 91	LATIN CAPITAL LETTER N WITH TILDE
Ò	c3 92	LATIN CAPITAL LETTER O WITH GRAVE
Ó	c3 93	LATIN CAPITAL LETTER O WITH ACUTE
Ô	c3 94	LATIN CAPITAL LETTER O WITH circumflex
Õ	c3 95	LATIN CAPITAL LETTER O WITH TILDE
Ö	c3 96	LATIN CAPITAL LETTER O WITH diaeresis
×	c3 97	MULTIPLICATION SIGN
Ø	c3 98	LATIN CAPITAL LETTER O WITH STROKE
Ù	c3 99	LATIN CAPITAL LETTER U WITH GRAVE
Ú	c3 the 9th	LATIN CAPITAL LETTER U WITH ACUTE
Û	c3 9b	LATIN CAPITAL LETTER U WITH circumflex
Ü	c3 9c	LATIN CAPITAL LETTER U WITH diaeresis
Ý	c3 9d	LATIN CAPITAL LETTER Y WITH ACUTE
Þ	c3 9e	LATIN CAPITAL LETTER THORN
ß	c3 9f	LATIN SMALL LETTER SHARP S
à	c3 a0	LATIN SMALL LETTER A WITH GRAVE
to	c3 a1	LATIN SMALL LETTER A WITH ACUTE
â	c3 a2	LATIN SMALL LETTER A WITH circumflex
ã	c3 a3	LATIN SMALL LETTER A WITH TILDE
ä	c3 a4	LATIN SMALL LETTER A WITH diaeresis
å	c3 a5	LATIN SMALL LETTER A WITH RING ABOVE
æ	c3 a6	LATIN SMALL LETTER AE
ç	c3 a7	LATIN SMALL LETTER C WITH CEDILLA
è	c3 a8	LATIN SMALL LETTER E WITH GRAVE
é	c3 a9	LATIN SMALL LETTER E WITH ACUTE
ê	c3 aa	LATIN SMALL LETTER E WITH circumflex
ë	c3 ab	LATIN SMALL LETTER E WITH diaeresis
ì	c3 ac	LATIN SMALL LETTER I WITH GRAVE
í	c3 ad	LATIN SMALL LETTER I WITH ACUTE
î	c3 ae	LATIN SMALL LETTER I WITH circumflex
ï	c3 af	LATIN SMALL LETTER I WITH diaeresis
ð	c3 b0	LATIN SMALL LETTER ETH
ñ	c3 b1	LATIN SMALL LETTER N WITH TILDE
ò	b2 c3	LATIN SMALL LETTER O WITH GRAVE
or	b3 c3	LATIN SMALL LETTER O WITH ACUTE
ô	c3 b4	LATIN SMALL LETTER O WITH circumflex
õ	c3 b5	LATIN SMALL LETTER O WITH TILDE
ö	c3 b6	LATIN SMALL LETTER O WITH diaeresis
÷	c3 b7	SIGN DIVISION
ø	c3 b8	LATIN SMALL LETTER O WITH STROKE
ù	c3 b9	LATIN SMALL LETTER U WITH GRAVE
ú	c3 ba	LATIN SMALL LETTER U WITH ACUTE
û	c3 bb	LATIN SMALL LETTER U WITH circumflex
ü	c3 bc	LATIN SMALL LETTER U WITH diaeresis
ý	c3 bd	LATIN SMALL LETTER Y WITH ACUTE
þ	c3 be	LATIN SMALL LETTER THORN
ÿ	c3 bf	LATIN SMALL LETTER Y WITH diaeresis

With this definition we are enabling identifiers as: “ícono”, “último”, ... but we will also be able “ñandu” (without accent), “être”, “÷b”, “Ça”.

This can include UTF-8 characters in different pages, but always including the entire page, not characters.

The following definition would give the same result:

  hlt.DefTokIdentif('[A-Za-zá]','[A-Za-z0-9]*');

But actually include UTF-8 pages 195 and 161, since the character "á" will be interpreted as two characters: 195 and 161. Therefore, this definition is not recommended.

For these characters, whether it is advisable to define the possible values ​​indicating the valid characters:

  hlt.DefTokIdentif('[A-Za-z'#195']','[áéíóúÁÉÍÓÚA-Za-z0-9]*');

This definition would be most appropriate to accept accented vowels as part of identifiers.

However, by the nature of UTF-8 (two bytes per character) and the nature of highlighter (one byte per character), this definition is not accurate, because there will always process the following bytes as if they were characters and groups of two characters .

Despite this semantic difference, the highlight will work pretty well, because divide the UTF-8 characters in two characters and consider both characters as valid. But would also pass (partly, only the first byte) characters of the page $89, $81, $8D, ...

Although you can define identifiers many pages of UTF-8, you can not define special identifiers of any UTF-8 page (see Section 5.5.2 - Special Identifiers)

## Special Identifiers

Special identifier can be added by code, using the method AddIdentSpec(), as shown in the following example:

  hlt.AddIdentSpec('IF', hlt.tnKeyword);

The first parameter is the identifier to add. This text must be strictly an identifier, ie it must meet the definition of identifiers. For example you can not define the word "$INCLUDE" as a special identifier, if the character $, not part of the initial valid characters for an identifier.

The case (uppercase or lowercase) of the identifier shall not be taken into account by default, unless the "CaseSensitive" property is set to TRUE in the highlighter.

The initial characters for special identifiers can only be English alphabetic characters, and characters _, $,%, @ and &. You can not use other characters that are not in this group.

You can assign any attribute to the special identifiers. The following example creates the special identifier “PI, ”with the attribute number:

  hlt.CaseSensitive : = true;
  hlt.AddIdentSpec('PI', Hlt.tnNumber);

In applying this definition, all identifiers "PI" is painted on the screen with the attributes configured in "hlt.tkNumber".

In this example, is set to read all identifiers considering its case. Therefore identifiers "Pi" and "pi" is not highlighted as numbers.

If we have reserved words already defined, we must first clear the memory, using the ClearSpecials() method:

  hlt.ClearSpecials;
  ...
  hlt.AddIdentSpec('PI', Hlt.tnNumber);
  hlt.AddIdentSpec('EPSILON', Hlt.tnNumber);
  ...

The AddIdentSpec() method lets you add special identifiers, one by one. To add multiple identifiers group must use the AddIdentSpecList () method:

  hlt.ClearSpecials;
  ...
  hlt.AddIdentSpecList('Begin end if', Hlt.tnKeyword);

The identifiers in the list must be separated by at least one blank.

As the keywords (attribute tkKeyword) are very common, there is a special method to add reserved words: AddKeyword().

  hlt.AddKeyword('Array');

The attributes of the keywords are changed using the "KeywordAttribute" property of the highlighter.

It is advisable not to include a large number of special identifiers, because you can get a deterioration in performance highlighter.

The special identifiers can be added dynamically, according to the needs of language. No need to make additional settings. What we can not do (at least directly) is to eliminate special identifiers that have been added.

The special identifiers added, should not be repeated, otherwise an internal error is generated and the instruction is ignored.

While the order in which identifiers are added, does not affect the syntax, if you can affect the performance of highlighter. For faster processing, we recommend putting words in the language are most likely to appear first.

Noting the declaration of AddIdentSpec (), we see that it has an additional parameter:

procedure AddIdentSpec(iden: string; tokTyp: integer;
        TokPos: integer=0);

The "TokPos" parameter allows us to indicate the order in which you must find the token to be considered as a special identifier.

In the following definition, we condition to which the identifier "START", is considered as a special token, only when it appears as the first token of the line.

  hlt.AddIdentSpec('START', Hlt.tnKeyword, 1);

In any other position, in which the token is found, it will be considered as a special identifier.

Likewise it may indicate that the token occupy the 2, 3 or any other. The first token to appear in a line will always be number 1, and so on. Do not forget that even the spaces are also a token.

By default, the value of "TokPos" is zero, which means it does not consider the order to occupy the token. But in defining "TokPos", you are giving a parameter, so that may be in the highlighter, two special identifiers with the same string but different token position. That is, the following definition will not generate error:

  hlt.AddIdentSpec('HOME', Hlt.tnKeyword, 1);
  hlt.AddIdentSpec('HOME', Hlt.nkKeyword, 2);

However, the following definition will fail, since there is a crossing in the definitions:

  hlt.AddIdentSpec('HOME', Hlt.tnKeyword 1);
  hlt.AddIdentSpec('HOME', Hlt.tnKeyword);

### Special identifiers in UTF-8

You can also define special identifiers with UTF-8 characters. To do this you must first have defined identifiers allow UTF-8 characters (See section on identifiers).

However, it is only possible to define special identifiers starting with a character of the UTF-8 code page $C3. This is because to process the special identifiers, you need to have a table created statically to quickly process the search words.

Fortunately, the code page $C3, covers all characters of Spanish and other Latin languages, such as Portuguese and French

To define special identifiers with extended characters, it is done in the same way as is done for other identifiers.

In the following code, identifiers that accept Spanish characters, are defined; and the keywords “uña” and “ñandú” are defined:

  hlt.ClearSpecials;
  hlt.ClearMethodTables;
  hlt.DefTokIdentif('[A-Za-z'#195']','[ÁéíóúñÑÁÉÍÓÚA-Za-z0-9]*');
  hlt.AddKeyword('uña');
  hlt.AddKeyword('ñandú');
  hlt.Rebuild;

This code produces the following result on a sample text:

One limitation with special identifiers with extended characters in UTF-8, is that you can not ignore the case. In the current version of SynFacilSyn, the "CaseSensitive" option enabled is not supported. All comparisons were made literally.

Do not forget that SyFacilSyn, will continue making comparisons using bytes, and in UTF-8, the extended characters are two bytes. Thus, as indicated:

  hlt.AddKeyword('uña');

We are entering a string of 4 bytes. And the comparison will always comparing the 4 bytes. That is why it is a bit complicated to ignore the case with UTF-8.

## Defining Tokens by content

Tokens for content defined in various ways. The easiest way is similar to how the identifiers are defined, but specifying the type of token:

  hlt.ClearMethodTables;
  ...
  hlt.DefTokContent('[0123456789]','[0-9]*', hlt.tnNumber);

In this example assumes that "hlt" is the highlighter. The "ClearMethodTables" instruction is necessary to clean the method table of the highlighter. "hlt.tnNumber" is the token type to which belong the tokens that meet this definition.

The method DefTokContent() allow us to define tokens by content. Its definition is:

  procedure DefTokContent(dStart, Content: string;
        typToken: integer ; Complete:boolean = false);

The "dStart" parameter defines the starting delimiter, or the list of valid characters to be the first character for the token by content. The "Content" parameter defines how the following characters, will be captured. Both parameters are expressed as regular expressions.

The parameter “typToken” defines the type of token. The parameter “Complete” is used to define if the token to extract must match the entire expression or may partially match.

Only 4 definitions of tokens by content (other from identifiers), are supported for the same syntax.

Another example would be this:

  hlt.ClearMethodTables;
  ...
  hlt. DefTokContent('[$]','[A-zA-Z0-9]*', tnDirective);

We can also specify a string as the starting delimiter. For example the following definition can recognize hexadecimal numbers in C language:

  hlt.DefTokContent('Ox','[0123456789]*', Hlt.tnNumber);

The first parameter of DefTokContent(), can only be a literal string or a list of characters (in brackets). Any other expression will generate an exception. When it is a string, it behaves as a delimiter, therefore must follow the rules of delimiters explained in section 3.5 - Token Delimiters.
Furthermore it must be remembered that an delimiter of identifier type, is affected by the "CaseSensitive" flag. In this sense the "dStart" parameter does not behave like a true regular expression. Therefore the definition:

  hlt.DefTokContent('Ox', '[0-9A-Fa-f]*', hlt.tnNumber);

Will coincide both with "0xFF" as with "0XFF" if the flag "CaseSensitive" was FALSE.
The second parameter of DefTokContent() may be a more complex regular expression (within the highlighter is supporting). For example to recognize decimal numbers, we can indicate:

  hlt.DefTokContent('[0-9]', '[0-9]*[\.][0-9]*', hlt.tnNumber);

"12", "12.3", "0.23": With this definition, the whole numbers and decimals are recognized.
Note that the decimal-point character has been escaped, because the "." Character has special meaning in regular expressions.

### Tokens matching

The matching of the tokens is done by parts. The starting delimiter, must first be match to start the processing of the token. Once the recognition of the special delimiter, it will become a recognized token. The "Content" parameter will extend the token to where the definition is matching. This means that the entire definition does not have to be matched for the token is recognized.
That is why the above definition, can recognize both whole numbers as decimal numbers. But even recognize the value and number "123" because it also meets the definition in part, until: '[.\]'

If you want the full definition of the token is fulfilled to take the token, you must put the "Complete" parameter to TRUE:

   hlt.DefTokContent('[0-9]', '[0-9]*\.[0-9]+', hlt.tnNumber, true);

With this definition, if the string "123" is found, only the first character of the token (character "1"), excluding the following characters[6], will be recognized because they do not fully meet the regular expression "Content" .
[6] Actually, the following characters are recognized as part of other tokens, eventually taking four distincs tokens "1", "2", "3" and ".".

For a token is fully recognized, with this definition, must necessarily include a decimal point.

It can be said that the "Complete" parameter allows exploration back to the point immediately after recognizing the starting delimiter. The initial delimiter will always be part of the token, once it is captured. Otherwise it could generate an infinite loop.

It is generally recommended to work with the "Complete" parameter to FALSE, to avoid unexpected results. If a better control of extracting tokens is desired, we recommend using the advanced definitions of tokens by content.

### Advanced definitions

The simplest form of the method DefTokContent() does not allow much control over the token to extract. For example if we process the token "1.2e-3", but only found the string "1.2e", for to extract only the part "1.2" we need a more flexible control on how to extract the tokens.
For this purpose, there is an alternative form of DefTokContent(), which can perform the same function as the simple form of DefTokContent().
Consider the following definition:

 hlt.DefTokContent('[0-9]', '[0-9]*\.[0-9]+', hlt.tnNumber);

This token can be expressed in the extended way:

uses ... , SynFacilBasic;
var
 p: tFaTokContent;
...
 p := hlt.DefTokContent('[0-9]', hlt.tnNumber);
 p.AddInstruct('[0-9]*');
 p.AddInstruct('\.');
 p.AddInstruct('[0-9]+');

Note that for to use the "tFaTokContent" type, in must be included the unit "SynFacilBasic".

In principle, this form is equivalent to the simplified version, only here the regular expression is added by parts, and also a "tFaTokContent" object is used.

The "tFaTokContent" object represents a definition of token by content. The AddInstruc() method is used to add an instruction, to the token by content. Each instruction includes a portion of the regular expression that defines the token.

The advantage of using the AddInstruc() method, to build the regular expression is further, we can add flow control instructions. Looking at the definition of AddInstruc(), we see:

procedure tFaTokContent.AddInstruct(exp: string; ifTrue: string='';
  ifFalse: string='';
  atMatch: integer=-1;
     atFail : integer=-1);

The parameters “ifTrue” and “ifFalse”, are strings that allow us to add simple instructions to control the flow of the token extractions.

The supported instructions are:

INSTRUCTION	DESCRIPTION
next	Jump to the next instruction.
exit	Ends the scan.
exit(n)	Ends the scan, and jump “n” instructions before exit. “n” can be positive or negative.
move(n)	Move the scan “n” instructions. “n” can be positive or negative.

Only one instruction can be included in the "ifTrue" and "ifFalse" parameters. The instruction given in "ifTrue" will run if the string matches the expression scanned, otherwise the instruction given in "ifFalse" run.

Instruction default for "ifTrue" is "next", meaning that if it matches the expression, simply go to the next instruction.

Instruction default for "ifFalse" is "exit", meaning that if doesn't match the expression, the scanning will be terminated and the token is recognized to that point.

An example of definition of tokens for content using instructions could be:

  p := hlt.DefTokContent('[0-9]', hlt.tnNumber);
  p.AddInstruct('[0-9]*');
  p.AddInstruct('\.',);
  p.AddInstruct('[0-9]+','','exit(-1)');

The "exit (-1)" statement in the final line indicates that if the expression '[0-9]+' is not met, the sacnning should jump to the start point of the previous instruction, ie, even before search the decimal point. Thus the extension of the token is corrected, if the decimal point is not found, to avoid to extract an erroneous token.

The parameter "exit" is always displayed as a signed displacement with respect to the current position. If no parameter is specified, "exit" simply exit without moving the position of current exploration, which is before (if the comparison fails) or after (if the comparison succeeds) to recognize the expression indicated in AddInstruc().

With this definition, it is possible to correctly recognize integer numbers and decimals. The following extraction cases apply to this definition:

String = “1”	-> Extract “1”
String = “123”	-> Extract “123”
String = “123.”	-> Extract “123”
String = “123.0”	-> Extract “123.0”

The "move" instrcution, always includes a parameter that indicates the next instruction to be executed. If such an instruction is indicated as:

  p.AddInstruct('hello','move(+2)','move(-1)');

What is meant is that if the comparison is true, the flow will jump two instructions below. Otherwise the next instruction to execute will be the last.

The parameter os move(), is always displayed as a signed displacement. "move(+1)" is equivalent to the "next" instruction.

We must be cautious when using the "move" command, because we can attempting to jump to nonexistent positions, or we can generate infinite loops.

The following example shows how we can write a definition for recognizing integer, decimal and scientific notation numbers in the same definition of token:

  p.AddInstruct('[0-9]*');
  p.AddInstruct('[\.]','','move(+2)');
  p.AddInstruct('[0-9]+','','exit(-1)');
  p.AddInstruct('[eE]');
  p.AddInstruct('[+-]?');
  p.AddInstruct('[0-9]+','','exit(-2)');

This definition will recognize correctly, the forms:

“1”
“12”
“1e2”
“1e+2”
“1.23”
“1.23e-5”

But will reject these incomplete forms:

1.”	-> Only extracts “1”
1e”	-> Only extracts “1”
“1.23e”	-> Only extracts “1.23”
1.23e+”	-> Only extracts “1.23”

This definition will behave better that the common definition:

 hlt.DefTokContent('[0-9]', '[0-9]*[\.][0-9]+[eE][+-]?[0-9]+');

Because, this last definition will recognize too, the strings “1.” o “1e”.

As an additional facility, it's possible to change the value of the initial token attribute, which was specified with DefTokContent (), using the "atMatch" and "atFail" parameters of AddInstruct(). So we have greater flexibility to determine the attribute assigned to the current token.

In the following code, we modify the previous example to differentiate integer from decimal numbers, verifying whether or not the decimal point:

  p := hlt.DefTokContent('[0-9]', hlt.tnNumber);
  p.AddInstruct('[0-9]*');
  p.AddInstruct('\.');
  p.AddInstruct('[0-9]+','','exit(-1)', tnDecimal);

What we do here, is tell the highlighter if the last statement is true, will end with the tnDecimal attribute, instead of tnNumber. We are assuming that the tnDecimal attribute has been previously created.
Likewise you can specify a different attribute in the event that the condition fails, using the "atFail" parameter.
To change the attribute of a token "on the fly", gives us great flexibility to handle complex definitions of tokens and frees us from the restriction that had with the other definitions, when the first character, always defined the attribute type that token.

## Special Symbols

The special symbols can be added by code using the AddSymbSpec() method, as shown in the following example:

  hlt.AddSymbSpec('+', tnOperator);

The first parameter is the command to add. This text must be a symbol, ie it must meet the definition of symbols. For example you can not define the word "$$" as a special symbol, if the character $, not part of the initial characters valid for a symbol (could have been assigned identifiers).

The case (uppercase or lowercase) symbol shall not be taken into account by default, unless the "CaseSensitive" property is set to TRUE in the highlighter. However, the effect of "CaseSensitive" is not often seen, because the symbols do not usually include alphabetic characters.

The second parameter is the type of token. It can be one of the predefined or any other that we have created. In this example, we assume that we have created the "tnOperator" type.

Type can be assigned to special tokens. The following example creates the special symbol "+A" to the type tnString:

  hlt.CaseSensitive : = true;
  hlt.AddSymbSpec('+A', hlt.tnString);

In applying this definition, all symbols "+A", will be painted on the screen with the attributes configured in "tkString". This definition can cause conflicts if texts as "B+A" is analyzed, since by definition the "+A" portion is considered as a single token with "tkString" attribute.

If you have previous special symbols defined, you must first clear the memory, using the ClearSpecials() method[7]:
[7] ClearSpecials () also removes the special identifiers. So be executed before creating both special identifiers special symbols.

  hlt.ClearSpecials; //clean identifiers and special symbols
  ...
  hlt.AddSymbSpec('+', tnOperator);
  hlt.AddSymbSpec('-', tnOperator);
  ...
  hlt.Rebuild; //necessary to complete the definition

Rebuild() method updates the table and sort the internal table of special symbols so that they can be correctly and quickly detected in the scan. Further processing blocks delimited tokens.

As is standard practice to always make Rebuild() at the end of the language definition.

The AddSymbSpec() method lets you add special symbols, one by one. To add multiple symbols in a group must use the AddSymbSpecList () method:

  hlt.ClearSpecials;
  ...
  hlt.AddSymbSpecList('+ - * / <> =: =', tnOperator);

The symbols on the list must be separated by at least one blank. Therefore, this definition does not allow you to create special symbols including the space character.

It is advisable not to include a large number of special symbols, because you can get a deterioration in performance highlighter. The search for special characters is not as optimized as special identifiers.

Special symbols added, should not be repeated, otherwise an internal error is generated and the instruction is ignored.

The order in which the special symbols are added, is not as important in performance, because the special symbols suffer a prior arrangement with RebuildSymbols().

The AddSymbSpec() method has an additional parameter:

procedure AddSymbSpec(symb: string; tokTyp: integer;
        TokPos: integer=0);

The "TokPos" parameter allows us to indicate the order in which you must find the token to be considered as a symbol Special.

In the following definition, we condition that the symbol ".", Is considered as a special token, only when it appears as the first token of the line.

  hlt.AddSymbSpec('.', hlt.tnKeyword 1);

In any other position, in which the token is found, it will not be considered as a special symbol.

Likewise it may indicate that the token occupy the 2, 3 or any other. The first token to appear in a line will always be number 1, and so on. Do not forget that even the spaces are also a token.

By default, the value of "TokPos" is zero, which means it does not consider the order to occupy the token. But in defining "TokPos", you are giving a parameter, so that may be in the highlighter, two special identifiers with the same string but different token position. That is, the following definition will not generate error:

  hlt.AddIdentSpec('.', hlt.tnKeyword, 1);
  hlt.AddIdentSpec('.', hlt.tnKeyword, 2);

However, if the following definition will fail, since there is a crossing in the definitions:

  hlt.AddIdentSpec('.', hlt.tnKeyword, 1);
  hlt.AddIdentSpec('.', hlt.tnKeyword);

## Definition of Delimited Tokens

Defined with DefTokDelim() method, which has the following declaration:

 procedure DefTokDelim(dStart, dEnd: string;
   tokTyp: integer;
   typDel: TFaTypeDel=tdUniLin; havFolding: boolean=false;
   chrEscape: char=#0);

The "dStart" and "dEnd" parameters are token delimiters. The "tokTyp" parameter indicates the type or attribute token. Optional parameters allow to configure whether the token is multiline or not, whether to include code folding and if a escape character is defined.

A simple case for string definition would be:

  hl : = TSynFacilSyn.Create(nil);
  SynEdit1.Highlighter : = hl;
  hl.DefTokDelim('"','"', hl.tnString);
  hl.Rebuild;
...

The Rebuild () method, must be run, always, after entering all tokens delimited, otherwise the definition will not effect.

This statement, assigns the "tkString" attribute to the string that is between single quotes, including the single quotes.

If we want the strings can be extended for more than one line and also can fold, the following code will work:

...
  hl.DefTokDelim('"','"', hl.tnString, tdMulLin, true);
  hl.Rebuild;
...

A text with this highlighter, could be shown as follows:

The code folding option is only valid when multi-line tokens are handled.

If the final delimiter of a delimited token is not specified, or is assigned the empty string, is assumed to extend to the end of the current line. This behavior is common in defining single-line comments. The following code creates strings and single-line comments in syntax highlighter:

...
  hl.DefTokDelim('"','"', hl.tnString);
  hl.DefTokDelim('//','',hl.tnComment);
  hl.Rebuild;
...

The attributes that can be assigned, are all who has defined the highlighter or any other created.

You can define as many delimited tokens as you want, considering that more of them, the greater the processing that should do the highlighter. The tokens with a character delimiters are those that are processed faster.

Strings and comments are classic examples of delimited tokens.

When defining delimited tokens, should be considered that a token delimiter is not the same delimiter for another token. Otherwise an internal error is generated and the definition, that conflicts will be ignored.

The delimiters of a token, are generally of symbol type, but may also be of identifier type (see Section 3.5 - Token Delimiters).

An example of delimited token, using identifiers can be:

  hl.DefTokDelim('REM','',hl.tnComment);

This syntax is for comments in the language of DOS Batch files, starting with the keyword REM and extend to the end of the line.

## Escape character

The "chrEscape" parameter allows you to specify a special character to be used as an escape character for delimited tokens. The following code shows how to define the "\" as an escape character for a string definition.

   hlt.DefTokDelim('"','"', hlt.tnString, tdMulLin, false, '\');

For definitions, with an escape character, take effect, observe that the start and end delimiters must be equal and of one character wide.

## Considerations of delimited tokens

When symbols are used, it should be noted that the "dStart" and "dEnd" parameters are receive
d in the form of regular expressions, with the limitation that "dStart" can only be a string literal or a simple list of characters, and "dEnd" can only be string literal. The following example defines a string beginning with quotes or the character "#":

  hl.DefTokDelim('["#]','"',hl.tnString);

Moreover, as the characters "*", "?", "+", "." And "\" have special meaning in regular expressions must be escaped. So to define C style comments (/ * ... * /) would:

  hl.DefTokDelim('/\*','\*/', hl.tnComment, tdMulLin);

If we introduce directly '/ *' in "dStart" will be interpreted as an expression of a character with quantifier, and an exception is generated, because "dStart" does not allow such expressions.

By defining a delimited token, "token delimiters" are specified too in the definition. A token delimiter is a special token (an identifier or symbol), which is used to identify a delimited token.

The following statement defines a token string from two identifiers:

  hl.DefTokDelim('Start','End', hl.tnString, tdMulLin);

By declaring "Start" as delimiter token, it is also defined the token "Start" as a special identifier and is defined with the property of “token by content”, so it loses its identity as a single token, and passes always be part of a larger token (with tkString attribute).

If the token "Start" has already been defined before, as a special token, its attribute is ignored and becomes a delimiter token. If it had not defined, it will be defined when creating the delimited token.

The token "End" is not created or updated as a special token. The search routines will find the identifier "End", by other means, without having to exist as a special token.

In fact, this search routine (for the end delimiter) is quite simple, so that makes an exact search, always considering the case. The "CaseSensitive" property has no effect in this case (see 6.11 - Limitations).

A final delimiter, for a delimited token, can be delimiter for other delimited tokens, but the starting delimiter is unique. There can not be two delimited tokens with the same starting delimiter. If a double definition is attempted, only take into account the latest.

When a multi-line token is created, there is the option to enable or code folding. And there is no greater difference in tokens with or without folding, except for the fold mark that appears when you create with code folding.

However, there is a difference. The tokens created with code folding, generate "code blocks" (see section 5.11 - Definition of block). Thus there are some additional properties that can be applied to these tokens. For more information see section 5.12 - Blocks as objects.

## Configuration Example

The following code creates a simple syntax for PHP:

procedure TForm1.FormCreate(Sender: TObject);
var
  hlt1: TSynFacilSyn;
begin
  hlt1 : = TSynFacilSyn.Create(self); //creates highlighter
  SynEdit1.Highlighter : = hlt1; //assigned to the editor
  hlt1.ClearSpecials; //to begin defining tokens
  hlt1.CreateAttributes; //Clean attributes
  hlt1.ClearMethodTables; //clean method table
  //tokens created by content
  hlt1.DefTokIdentif('[$ A..Za..z_]','[A-Za-z0-9_]*');
  hlt1.DefTokContent('[0..9.]','[0-9xabcdefXABCDEF]*','', Hlt1.tnNumber);
  //defined keywords
  hlt1.AddIdentSpec('__file__ ', hlt1.tnKeyword);
  hlt1.AddIdentSpec('__LINE__', hlt1.tnKeyword);
  hlt1.AddIdentSpec('Array', hlt1.tnKeyword);
  hlt1.AddIdentSpec('And', hlt1.tnKeyword);
  hlt1.AddIdentSpec('Break', hlt1.tnKeyword);
  //Alternatively declaration
  hlt1.AddIdentSpecList('Case class const continue ', hlt1.tnKeyword);
  hlt1.AddIdentSpecList('Default die do double ', hlt1.tnKeyword);
  hlt1.AddIdentSpecList('Elseif else echo empty endif endfor', hlt1.tnKeyword);
  hlt1.AddIdentSpecList('Eval endswitch endwhile exit extends', hlt1.tnKeyword);
  hlt1.AddIdentSpecList('Function false float for ', hlt1.tnKeyword);
  //Alternatively declaration
  hlt1.AddKeyword('Global');
  hlt1.AddKeyword('Highlight_file');
  hlt1.AddKeyword('Highlight_string');
  hlt1.AddKeyword('If');
  hlt1.AddKeyword('Int');
  hlt1.AddKeyword('Include');
  hlt1.AddKeyword('Integer');
  hlt1.AddKeyword('Isset');
  hlt1.AddKeyword('List');
  hlt1.AddKeyword('New');
  hlt1.AddKeyword('Object');
  hlt1.AddKeyword('Old_function');
  hlt1.AddKeyword('Or');
  hlt1.AddKeyword('Print');
  hlt1.AddKeyword('Real');
  hlt1.AddKeyword('Require');
  hlt1.AddKeyword('Return');
  hlt1.AddKeyword('Show_source');
  hlt1.AddKeyword('Static');
  hlt1.AddKeyword('String');
  hlt1.AddKeyword('Switch');
  hlt1.AddKeyword('True');
  hlt1.AddKeyword('Unset');
  hlt1.AddKeyword('Var');
  hlt1.AddKeyword('While');
  hlt1.AddKeyword('Xor');
  //creates delimited tokens
  hlt1.DefTokDelim('','', hlt1.tnString);
  hlt1.DefTokDelim('"','"', hlt1.tnString);
  hlt1.DefTokDelim('//',' ', hlt1.tnComment);
  hlt1.DefTokDelim('/ *','* /', hlt1.tnComment, tdMulLin);
  hlt1.Rebuild;
end;

In this syntax, only the treatment of tokens are defined. Only token types that already exist in the highlighter is used, no new types of tokens are created.

## Definition of blocks

The blocks can be understood as sets of consecutive tokens with syntactic meaning, clearly defined by delimiters, which are also tokens.

The easiest way to define blocks is using the AddBlock() method, which has the following declaration:

function TSynFacilSyn.AddBlock(
  dStart, dEnd: string;
  showFold: boolean = true;
  parentBlk: TFaSynBlock = nil;
): TFaSynBlock;

The description of the parameters is:

dStart	Mandatory	Initial boundary of the block. Must be a special token.
dEnd	Mandatory	Delimiter end of the block. Must be a special token.
showFold	Optional	Indicates whether the fold mark is displayed in the editor. This mark appears only when the block has more than one line. By default, it is enabled.
parentBlk	Optional	Indicates the parent of the block. The default is NIL, ie it is valid within any block or section.

A simple case of block definition would be:

  hlt.AddBlock('Begin','End'); //adds the block
...
  Rebuild;

The Rebuild() method, you must run, always, after entering all blocks, otherwise it may not effect the definition.

By default a defined block displays the fold mark:

The block will extend from the token "BEGIN" to the end of the token "END". The block may be distributed in one or more lines. Is not necessary to specify. The blocks are multiline by default.

If we want the block does not show the fold mark, we should explicitly indicate it in the third parameter:

  hlt.AddBlock('Begin','End',false);

Block delimiters can also be symbols. For example, the following statement is valid:

  hlt.AddBlock('(',')');

This definition, consider all tokens in parentheses as part of a block.

Block delimiters must always be special identifiers or special symbols. If it is used a delimiter of block that is not defined as a special token, it is first created as a special token before processing the block.

For example, in the following definition:

  hlt.AddBlock('Begin','End');

If the identifier "Begin" was not created as a special identifier, then first "Begin" will be created as a special token, within the highlighter, with the "tkIdentif" attribute.

If the special identifier already existed, it is not created again nor its attribute is changed.

It is noteworthy that the highlighter will always try to identify the block delimiters as a special identifier or a special symbol. The identification rule is simple:

If the first character of a delimiter (initial or final) is on the list of valid characters of an identifier, it is assumed that all the delimiter must be an identifier (For rules of token of identifier type). Otherwise an internal error will be generated.

For example the following code will fail when trying to run it, if the character “%” does not belong to the valid characters for an identifier:

  hlt.AddBlock('Begin%','End');

If the first character of a delimiter is not on the list of valid characters of an identifier, it is assumed that all the delimiter must be a symbol. No validations on the validity of the boundary as such be made. It is the responsibility of the programmer ensure this.

Consider for example the following definition:

  hlt.AddBlock('”Hey”','”You”');

The highlighter try to encode "hey" (including the quotes) as a special symbol, and could leave without effect, some previous definition of strings (that uses quotes).

You can define as many blocks as you want, considering that more of them, the greater the processing that should do the highlighter.

## Blocks as objects

Within the highlighter, the blocks are objects of the "TFaSynBlock" class, that have the following definition:

  TFaSynBlock = class //class to handle syntax blocks
    name : string; //block name
    index : integer; //indicates its position within TFaListBlocks
    showFold : boolean; //indicates whether the fold mark is displayed
    parentBlk : TFaSynBlock; //parent block (where the block is valid)
    Backcol : TColor; //background color of a block
    IsSection : boolean; //indicates whether a block of type section
    UniqSec : boolean; //Indica is only section
  end;

An important detail is that a block does not store a reference to the delimiters. The following section will explain more about this.

The blocks are created in the highlighter, by AddBlock() method.

Whenever used AddBlock(), are creating a new object "TFaSynBlock". The AddBlock() method is actually a function that returns a reference to "TFaSynBlock" object, which represents the block.

Having reference to the block object, allows us to access additional properties. In the following code, access to the object block is used to name the block:

var
  hlt : TSynFacilSyn; //object block
  bl_llaves: TFaSynBlock;
...
  bl_llaves : = hlt.AddBlock('{','}');
  bl_llaves.name: = 'Bloque_llaves'; //assigns a name

The name of block is not an important property when the highlighter is configured by code. This property is used by the highlighter, when the syntax with the XML file is configured.

There are two predefined highlighter, which are always created blocks. These are:

- MainBlk -> Identifies the main block. The one who has no nesting.
- MulTokBlk -> Refers to the blocks that represent to all the multi-line tokens that have enabled folding.

These block are common blocks, like any other, except that it need not be created or destroyed. With them you can change some properties of syntax.

The following code will disable code folding of all multiline tokens created or to be created; something that can not be done by XML file.

var
  hlt : TSynFacilSyn;
...
  //disables folding of all multiline tokens
  hlt.MulTokBlk.showFold: =false;
  //creates multiline token with folding that won't show folding mark
  hlt.DefTokDelim('/ *','* /', tnComment, tdMulLin, true);

This is possible because all the multiline tokens use the same predefined block MulTokBlk. So by changing the properties of "MulTokBlk", we are changing the properties of all blocks that form the multi-line tokens (that were created with folding).

## Advanced Blocks

The AddBlock() method allows us to create blocks in a simple form, indicating a single delimiter start and an end. But not allow us more flexibility to define delimiters.

There is an alternative way that allows us greater freedom. This involves using the method of creating blocks CreateBlock (), which has the following declaration:

    function CreateBlock(blkName: string;
        showFold: boolean=true;
        parentBlk: TFaSynBlock=nil): TFaSynBlock;

CreateBlock() allows us to internally create a block in the highlight (and their main properties) but without defining its delimiters.

Is it possible to have a block without delimiters? Certainly yes. However this block will not open in a normal highlighter exploration.

The common way in the highlighter works, is to configure the tokens that are delimiters, so they keep a reference to the block or section they open (may be more), and block they close (may be more). It is the exploration of tokens (no block) that determine when it opens or closes a block.

The blocks are stored in the memory of the highlighter, but they have no reference to any start or end delimiter (since there may be several tokens that open or close). Tokens are the delimiters, which keep the reference to blocks that open and close.

The diagram below will help to clarify the indicated:

For to associate the special delimiters, to one block, there are the functions AddIniBlockToTok() and AddFinBlockToTok(), that have the following statement:

    procedure AddIniBlockToTok(dStart: string; TokPos: integer;
        blk: TFaSynBlock);
    procedure AddFinBlockToTok(dEnd: string; TokPos: integer;
        blk: TFaSynBlock);

To appreciate the difference in blocks creation, consider the following statement block:

  blq_codigo : = hlt.AddBlock('Start','End');

And the alternative equivalently, using CreateBlock ():

  blq_codigo : = hlt.CreateBlock(''); //Create block
  //Assigns refer. block the token 'Start' wishlist 'blocks that opens"
  AddIniBlockToTok('Start', 0, blq_codigo);
  //Assigns refer. block the token 'End' in its list of "blocks that closes"
  AddFinBlockToTok('End', 0, blq_codigo);

The AddIniBlockToTok() method accesses to the list "BlksToOpen", of the special token, to add the reference to the indicated block. So when this token is identified, we will know it is the beginning of the block "blq_codigo". Likewise works AddFinBlockToTok() but with "BlksToClose" list.

This new block definition gives us more freedom to:

- Including the additional parameter "TokPos" in the delimiters.
- To include multiple delimiters.

The "TokPos" parameter specifies more detail regarding the delimiters. It allows us to fully identify a special token that has been declared by this parameter (See Section 4.5.2 and 4.4.1).

For example, using a definition like this:

  blq_codigo : = hlt.CreateBlock(''); //Create block
  AddIniBlockToTok('Start'2, blq_codigo);

Hopes to use as a starting delimiter, a special identifier that is declared like this:

  hlt.AddIdentSpec('Start', tnKeyword, 2);

If there is not this definition, it will proceed to create it, because the block require always the delimiters exist first as special tokens.

The alternative delimiters, definition allows us also, to define more than one start or end delimiter, for the same block.

For example if we want the BEGIN ... END block can also be open with the keyword START, then the statement would be:

  blq_codigo : = hlt.CreateBlock(''); //Create block
  AddIniBlockToTok('Begin', 0, blq_codigo);
  AddIniBlockToTok('Start', 0, blq_codigo);
  AddFinBlockToTok(End ', 0, blq_codigo);

Each call to AddIniBlockToTok(), will define an additional starting delimiter. The same applies to AddFinBlockToTok().

The AddIniBlockToTok() and AddFinBlockToTok() makes a verification of the validity of the delimiters, the same way to how it works AddBlock(). This means it is advisable to always check if an error occurs in the definition of the delimiters.

## Coloring of blocks

As an additional feature, the highlighter lets us to color the background of the blocks to provide a visual aid, to identify the blocks extension.

To activate the coloring of blocks, we must set the "ColBlock" property of the highlighter. Allowed values ​​are:

cbNull	Disables the colored blocks. It is the default option.
cbBlock	Color block background by level. Displays the blocks with a more or less dark, according to the level of the block or section color.
cbLevel	Block background colors using the color defined for each block, in his "BackCol" parameter. (See Section 4.10 - Block Definition)

The following code sample sets the colored highlighter by level:

var
    hlt : TSynFacilSyn;
begin
  hlt : = TSynFacilSyn.Create(self); //creates highlighter
  SynEdit1.Highlighter : = hlt;
  hlt.ColBlock: = cbLevel; //colored set
  hlt.AddBlock('{','}'); //creates block
  hlt.Rebuild;

When we set “ColBlock” to "cbLevel", it will proceed to do and automatic coloring of blocks, using the nesting level of each block. The following example shows how a simple C code would look with colored Level:

In this style colored, the innermost block will appear with both darker purple hue, the more nesting level has the block. The base color is not configurable per file or instructions, but can be changed by modifying the TSynFacilSyn.GetTokenAttribute () method in the code highlighter.

Note that when the colored blocks are active, the block delimiters are also considered as part of the block and also appear colored.

The blocks only allow you to change the background color of the tokens that are contained in the block (including spaces). When the colored block is activated, the "Background" property attributes tokens are ignored.

You can not change the text color or some other visual attribute of tokens within a block. These always correspond to what is defined in the attributes of the highlighter.

The other colored is colored by block. If we ColorBlock in "cbBlock" will be colored using as background color, the color defined for each block. The figure below shows how the same text would be using colored blocks.

This type of coloring, does not take into account the level of nesting, but uses the custom color that is specified in the definition of each block.

The background color of a block is specified in the "BackCol" property of the block. To change this property, you must have the reference to the object block:

var
  hlt : TSynFacilSyn;
  bl_llaves: TFaSynBlock; //object block
begin
  hlt : = TSynFacilSyn.Create(self); //creates highlighter
  SynEdit1.Highlighter : = hlt;
  hlt.ColBlock: =cbBlock; //colored active block individually.
  bl_llaves : = hlt.AddBlock('{','}'); //creates block
  bl_llaves.BackCol: =clYellow; //Set the background color of the block.
  hlt.Rebuild; //reconstructs

If not want to specify a particular color for a block without or want to use the color of the previous block, use the constant: COL_TRANSPAR:

  bl_llaves.BackCol: =COL_TRANSPAR; //Set transparent color.

It should be noted that by using the colored block work requires more processing in the highlighter, which when used for level highlighted.

## Scope of a block

The definition of a block is, by default, valid anywhere in the text. Thus, if we define the block:

  bl_llaves : = hlt.AddBlock('{','}');

This definition will always be valid, ie, whenever the highlighter find the special symbol "{", shall open the block "bl_llaves" and in the same way, each time it finds the symbol "}", proceed to close block.

So if we write C code with this syntax, we get the following image:

The image one can clearly see that the two blocks have been recognized in the syntax, although one of them is located inside the other. We could create countless nested blocks this way.

This is because in the block definition, have not specified the scope of the block in the "parentBlk" parameter, and this has taken the NIL value, which means that the block is valid anywhere where it appears.

The same result would have obtained had we explicitly since the block is valid anywhere using the following form:

  bl_llaves : = hlt.AddBlock('{','}',true,nil);

Using the "parentBlk" parameter, you can limit the validity of a block specific areas of code that can be other blocks or sections.

For example, the following definition creates first block "aquí_si" and then define the block "bl_llaves" to be valid only within this block:

  aqui_si : = hlt.AddBlock('Aqui_si','fin');
  bl_llaves : = hlt.AddBlock('{','}',true, Aqui_si);

A sample code will show the effect of this definition:

As shown, the second block is not recognized because it is outside of the block "aqui_si".

Be careful, to restrict a range block. Especially nested blocks can appear. For example if we define the block "Bl_llaves" to be valid only in the main block:

  bl_llaves : = hlt.AddBlock('{','}',true, Hlt.MainBlk);

We could have the following result:

And we note that the second key "{", found not open another block, because it is not within the main block. However the first key "}" found, recognizes itself as the final delimiter of the block, excluding some of the code and giving rise to an erroneous definition syntactically.

The "MainBlk" block, as we remember, is a predefined block highlighter, which includes the entire file. All tokens and blocks (or sections), believed to be directly or indirectly contained in the block "Main".

The interior of any block, is no longer part of the block "MainBlk". Only tokens or structures that are not within another block, pertain directly to the block "MainBlk"

It belongs to the block "MainBlk"
No belongs to the block "MainBlk"

When blocks are only valid in the block "MainBlk", they are preventing these can be nested and may appear only in the main body are created.

You can limit the nesting level of a block. This requires specifying the structure, each block corresponding to each level.

The following example is a definition to allow only two levels of keys:

  //valid block "MainBlk"
  bl_llaves : = hlt.AddBlock('{','}',true, Hlt.MainBlk);
  //valid block "bl_llaves"
  bl_llaves2 : = hlt.AddBlock('{','}',true, Bl_llaves);

Now with this definition, be permitted to include a block "{}", within another, but no more. Thus, if a third nesting can be included, fail syntax:

Note that that "bl_llaves" so that this definition to work properly, it is necessary, is defined only in the main block "MainBlk". Otherwise will have no effect, nesting limit we want.

## Defining sections

Defined with Addsection() method, which has the following declaration:

function TSynFacilSyn.AddSection(
  dStart: string;
  showFold: boolean = true;
  parentBlk: TFaSynBlock = nil;
): TFaSynBlock;

The description of the parameters is:

dStart	Mandatory	Initial boundary of the section. Must be a special token.
showFold	Optional	Indicates whether the fold mark is displayed in the editor. This mark appears only when the block has more than one line. By default, it is enabled.
parentBlk	Optional	Indicates the parent of the block. Default is NIL, which means that the section is valid in the main block.

A section parameters are similar to the parameters of a block, except that there is not the ending delimiter, because the blocks have another mechanism to determine an end.

Another important difference is that the default value NIL, the "parentBlk" does not mean "valid in any block", as in AddBlock(). Here NIL means that the section applies only in the main block. You can not define a section that is valid anywhere, because this would mean to have the same nested section, which goes against the definition of sections.

As the sections are also blocks most blocks rules apply also here. Coloring sections also is similar to the colored blocks.

A simple case of block definition would be:

  hlt.AddSection('Implementation');
...
  hlt.Rebuild;

This section will extend from after the token "interface" to the end of the program, if any other section is defined.

The Rebuild() method, must be executed, always, after entering all sections and blocks, otherwise it may not effect the definition.

You can define as many sections as you want, considering that more of them, the greater the processing that should do the highlighter.

If we define two sections, then we are dividing the code into two or more parts:

  hlt.AddSection('Interface');
  hlt.AddSection('Implementation');

Now we have that, an "interface" section may end at the begining of an "implementation" section, if there is one.

The following figure shows a sample code with the created sections:

The order in which the sections are defined is not important. Does not imply an order in recognizing sections. In our example the sections have been correctly recognized, and including a duplicate section.

To avoid that the same section, be recognized two or more consecutive times, use the property "UniqSec" of the block. If activated, it will not allow a repeat section after herself. This means that only recognize the first time it appears.

In our example does not allow the same section consecutively, we'd have:

var
  sec1, sec2: TFaSynBlock;
...
  sec1 : = hlt.AddSection('Interface');
  sec2 : = hlt.AddSection('Implementation');
  sec1.UniqSec: =true;
  sec2.UniqSec: =true;

The effect would be this:

As you can see, there is only one "implementation" section (see fold mark), since the latter is not regarded as a new section. However, if it is possible to define "implementation" section again, after an "interface" section.

The sections are often used to represent special code blocks in a programming language, such as sections "interface" and "implementation" Pascal. These language structures are not well suited to manage them as blocks.

The examples seen previously worked only in the main block, but sections can also work within other specific blocks. This is to segment regions of code within these blocks.

As an example consider the class declaration syntax in Pascal. In it, there may be the "private", "public" and "protected" sections.

To define these sections within the class declaration, we first define a block that includes the class, and then the inner sections.

  bloClas : = hlt.AddBlock('Class','End');
  hlt.AddSection('Private',true, BloClas);
  hlt.AddSection('Public',true, BloClas);
  hlt.AddSection('Protected',true, BloClas);

A class declaration text, would be as shown in the following figure:

## First Section

Sections usually begin, after the block that containing it, has begun. However, it may be that we need to open a section while a block is open.

This is what is called the "First Section". To understand this concept, consider the following structure:

SELECT field1,
field2
FROM
table1, table2
;

The task here would be represented by blocks and sections, the structure of the SQL query so that it has two folding parts. The first part would be from the word SELECT, even before the word FROM, and the other part would be from the word FROM until the end of the consultation.

The first solution would be to simply define two separate sections that begin with SELECT and FROM words. But if we wanted to keep the syntactic unit of full consultation, should be included in a block.

As a solution will raise the option of defining a block begins with the word Reserved SELECT and end with a semicolon:

  bloSelect: = hlt.AddBlock('SELECT',';');

In this way we manage the entire query as a block. But now we need to divide it into two sections. The FROM section offers no problem, because it is a common section.

However, the first section, which starts with SELECT, can not be defined directly as SELECT, it is also the starting delimiter of the block. If we tried to define it like this:

  bloSelect: = hlt.AddBlock('SELECT',';');
  hlt.AddSection('SELECT',true, BloSelect);
  hlt.AddSection('FROM',true, BloSelect);

The SELECT section would not open at the beginning of the consultation, because verification of sections, is made after recognizing the word SELECT.

To open the block, while a section, we set up a special section on the delimiter token. This is called "First Section".

To create a first section, use the AddFirstSection() method, which is similar to Addsection(), in his statement:

function TSynFacilSyn.AddFirstSection(
      dStart: string; showFold:
      boolean = true;
      parentBlk: TFaSynBlock = nil): TFaSynBlock;

With AddFirstSection(), we can tell the highlighter, indicated that the token (which should open a block), also open the indicated section.

Thus, the solution to our problem would be in the following code:

  bloSelect: = hlt.AddBlock('SELECT',';');
  hlt.AddFirstSection('SELECT',true, BloSelect);
  hlt.AddSection('FROM',true, BloSelect);

Now, when the block "bloSelect" opens, a section will appear. The effect is similar to that shown:

Now you have two collapsible sections within a block, which is also foldable, but that is not accessible with the mouse, by appear "under" the folding mark.
## Advanced sections

The method Addsection() allows us to create sections, in a easy way, indicating a simple start delimiter. But not allow us greater freedom to define this delimiter.

There is an alternative way that allows us greater freedom. This involves using the method of creating blocks CreateBlock (), which has the following declaration:

    function CreateBlock(blkName: string;
        showFold: boolean=true;
        parentBlk: TFaSynBlock=nil): TFaSynBlock;

CreateBlock() allows us to internally create a block or section in the highlight (and their main properties) but without defining its delimiters.

The way the highlighter works, is to configure the the tokens that are delimiters, so they keep a reference to the block or section that they open (may be more), and close (may be more). It is the exploration of tokens (no blocks) that determine when it opens or closes a section.

The sections are stored in the memory of highlighter (sharing the place with blocks), but they have no reference to a start or end delimiter (since there may be several tokens that open or close). The Tokens delimiters, are who keep the reference to the sections that open and close.

The diagram below will help clarify as indicated:

Technically, there is no tokens that keep references to sections that they close. The sections are closed automatically when there is another section in the same level or end of the block that contains it (See 3.7 - Sections).

To associate special delimiters, to a section, there is AddIniSectToTok() method, which has the following declaration:

  procedure AddIniSectToTok(dStart: string; TokPos: integer; blk: TFaSynBlock);

To appreciate the difference in creating sections, consider the following statement:

  sec1 : = hlt.AddSection('Interface',true, Hlt.MainBlk);

And the alternative equivalently, using CreateBlock():

  sec1 : = hlt.CreateBlock('',true, Hlt.MainBlk); //Create block
  sec1.IsSection : = true; //mark as section
  //Assigns section to the token 'interface', in its list of "sections that opens"
  AddIniSectToTok('Interface', 0, sec1);

Here we can see better that a section is a simple block, but with the "IsSection" property set to TRUE. This will do that the highlight try to this block, on a different form.

IMPORTANT. By creating sections AddBlock, must take into account two considerations:

- Always put the IsSection property to TRUE.
- Always specify the parent block. Leave the default (NIL), the section will not be recognized

The AddIniSectToTok() method accesses to the list "SecsToOpen" of the special token, to add the reference to the indicated block. So when it's identified this token, we will know that it is the beginning of the Section 'sec1 ".

This new block definition gives us more freedom to:

- Include the additional parameter "TokPos" in the start delimiter.
- Include multiple start delimiters.

The "TokPos" parameter allows us to specify more detail about the start delimiter. It allows us to fully identify a special token that has been declared with this parameter (See Section 4.5.2 and 4.4.1).

For example, using a definition like this:

  sec_clase : = hlt.CreateBlock('' true, hlt.MainBlk); //Create block
  sec_clase.IsSection : = true; //mark as section
  AddIniSectToTok('Private'1, sec_clase);

Hopes to use, as a starting delimiter, a special identifier that is declared like this:

  hlt.AddIdentSpec('Private', tnKeyword 1);

If there is not this definition, it proceeds to create it, because the block (section) always requires that the delimiter exists first as a special token.

The alternative definition for delimiters also allows us to define more of one starting delimiter, for the same section.

For example if we want the previous section can be open using the keyword "private2" then the statement would be:

  sec_clase : = hlt.CreateBlock('' true, Hlt.MainBlk); //Create block
  sec_clase.IsSection : = true; //mark as section
  AddIniSectToTok('Private', 0, sec_clase);
  AddIniSectToTok('Private2', 0, sec_clase);

Each call to AddIniSectToTok(), will define an additional starting delimiter. There may be as many as desired.

The AddIniSectToTok() method, makes a validation for the delimiter, in the same way that Addsection() works. This means that it is advisable to always check if an error occurs in the definition of the delimiter.

This method of creating sections, also allows us to define "First Sections", using the method: AddFirstSectToTok(), as does AddFirstSection().

## Getting information about blocks

The highlighter TSynFacilSyn, can define blocks that can be colored or folded. But for better benefits, it is needed to access to internal information on these blocks.

To this end, we have defined the following methods:

### SetHighlighterAtXY()

It has the following statement:

function SetHighlighterAtXY(XY: TPoint): boolean;

This method allows to locate the highlighter in a specific position of the text. It's like if you were doing the normal scan text and stops at the position indicated.

This is useful because it allows us to read the status of highlighter when reached anywhere in the text. So we can see information about tokens and blocks.

The XY parameter indicates the position of the text where you want to put the highlighter. These are values ​​that start at 1 for the first row or first column. The following example shows how you can put the highlighter in the position where the cursor is, in an editor SynEdit1:

  SynFacilSyn1.SetHighlighterAtXY(SynEdit1.CaretXY); //positions
  //from here you can get information about the highlighter
  tok : = SynFacilSyn1.GetToken; //reads the current token

This example takes to read the token under the cursor, but the same could have done with TSynEdit.GetHighlighterAttriAtRowCol(). However SetHighlighterAtXY(), only positions the highlighter, from there, you can read all available information. GetHighlighterAttriAtRowCol() gives only information about the token and attribute. Furthermore SetHighlighterAtXY(), is optimized for TSynFacilSyn and is therefore faster.

Internally SetHighlighterAtXY(), takes a little exploration, but only in the line of work. No need to be explored throughout the text, because the highlighter status information, is saved internally for each line.

### NestedBlocks ()

It has the following statement:

function NestedBlocks: Integer;

This function returns the number of currently open blocks. This value can be read at any time, but usually will be used after calling SetHighlighterAtXY() to see the open blocks in any position of the text.

The following example shows how to read the nesting level at the cursor position:

  SynFacilSyn1.SetHighlighterAtXY(SynEdit1.CaretXY); //positions
  level : = SynFacilSyn1.NestedBlocks; //read nesting

There is, in the TSynCustomFoldHighlighter class, the FoldBlockEndLevel() method, that also returns the number of open blocks, but only give this information to the end of a line and does not consider either all the blocks but only those with code folding.

### NestedBlocksBegin ()

It has the following statement:

function NestedBlocksBegin(LineNumber: integer): Integer;

This function returns the number of open blocks at the beginning of a line.

Unlike NestedBlocks(), this method need not be positioned first in the text, using SetHighlighterAtXY(). Simply you must pass as a parameter the line number and the function returns the number of open blocks, when starting a line scanning.

This value is obtained by reading the state of the end of the line to the previous line, accessing information ranges.
### TopCodeFoldBlock()

It has the following statement:

function TopCodeFoldBlock(DownIndex: Integer): TFaSynBlock;

This function returns the last open block on the highlighter. The "DownIndex" parameter indicates the depth of the requested block. When is 0, refers to the last open block; when one refers to the penultimate, and so on.

The same information could be obtained with TSynCustomFoldHighlighter.TopCodeFoldBlockType() method, but it is inaccessible from outside the class, andTopCodeFoldBlock() returns directly an object TFaSynBlock.

When the current block is the main block, that is, there is not any block open, TopCodeFoldBlock() returns NIL.

The following code shows how to read the name of the last open block at the cursor position:

  SynFacilSyn1.SetHighlighterAtXY(SynEdit1.CaretXY); //positions
  blk : = TopCodeFoldBlock(0); //read current block
  if blk <> nil then nombre_bloque : = blk.name;

### GetBlockInfoAtXY()

It has the following statement:

function GetBlockInfoAtXY(XY: TPoint; out blk: TFaSynBlock; out level: integer): boolean;

This method allows us to obtain the latest open block, for any position of the text. It returns the number of open blocks in that position, in the parameter "level".

It job is simple, since only places the highlighter at the indicated position, and there reads the information from the last block, using TSynCustomFoldHighlighter.TopCodeFoldBlockType().

It is a shorthand way to access the active block in a text position.

The XY parameter indicates the position of the text where you want to read the block. These are values that start at 1 for the first row or first column.

The following example shows how you can read the name of the current block, where the cursor of a SynEdit1 editor is:

var
  blq: TFaSynBlock;
  level: integer;
...
  SynFacilSyn1.GetBlockInfoAtXY(SynEdit1.CaretXY, blq, level);
  if blq = nil then
    debugln('Block= NIL, Level='+IntToStr(level))
  else begin
    debugln('Block=' + blq.name+'Level='+IntToStr(level));
  end;

### ExploreLine()

It has the following statement:

function ExploreLine(XY: TPoint; out toks: TATokInfo; out CurTok: integer): boolean;

This method performs a scan of the line in "XY", and read detailed information of tokens at that line, also indicating what is the token in the "XY" position.

The TATokInfo type, is an aray of elements of type TFaTokInfo:

  TFaTokInfo = record
     txt : string; //Token text
     TokPos : integer; //Token position within the line
     TokTyp : integer; //token type
     posIni : integer; //starting position on the line
     curBlk : TFaSynBlock; //Token reference to block
  end;

  TATokInfo = array of TFaTokInfo;

The TFaTokInfo structure contains all the information relating to a token that may be needed in a typical scan text.

After a call to ExploreLine(), the tokens of the line in "XY", are returned in the toks[] parameter. This array start at index 0.

The CurTok parameter indicates the position within toks[], corresponding to the token that is below the "XY" coordinate. So you can easily locate the token of the current position.

This feature was designed thinking on easing the implementation of the “completion code” option, using information from tokens and blocks of the highlighter.

The functions SearchBeginBlock(), SearchEndBlock() are extensions that are still in development, so should not be used yet.

## Using the highlighter as lexical analyzer - syntactic

The TSynFacilSyn highlighter is not only a highlighter for SynEdit component, but is also an excellent configurable lexical analyzer (lexer).

It behaves like a scanner, because once configured to one syntax, it can extract each of the tokens in the source text.

Scanning can be done in a single line or an entire multiline text.

Note that to use SynFacilSyn, necessarily requires SynEdit package even if you do not intend to use any component of SynEdit.

### Scanning in a line

The extraction of tokens is done according to the syntax that has defined the highlighter. Do not forget that a highlighter SynFacilSyn, always carries a syntax defined by default. But if this does not meet the requirements, you must first configure the appropriate syntax.

To scan a line of text, simply call setline () with the line to be analyzed.

you use ..., SynHighlighterFacil;
xLex : = TSynFacilSyn.Create(self);
// Define the syntax
...

  // Explores
xLex.SetLine('Somewhere in the spot', 0);
while not xLex.GetEol do begin
//here is pointing to a token
    Token : = xLex.GetToken; //reads the token
    TokenAtt : = xLex.GetTokenAttribute; //read attribute

    //passes to the next
xLex.Next;
end;

The second parameter setline() is the line number that is being explored, but for our purposes it is not important, so we left at zero.

The text of the token is read with GetToken() method. It is a simple string with the text of the current token.

We can also use the highlighter to extract text fragments, if these can be defined as tokens. In the following example, used the highlighter to extract the strings that are in parentheses.

uses ..., SynEditHighlighter, SynHighlighterFacil;
  xLex : = TSynFacilSyn.Create(self);
 // Define the syntax
 xLex.DefTokDelim('(',')', xLex.tnKeyword);
 xLex.Rebuild;

 // Explores
 xLex.SetLine('123(abc)345(def)000', 0);
 while not xLex.GetEol do begin
   if xLex.GetTokenKind = xLex.tnKeyword then
      ShowMessage(xLex.GetToken);
   xLex.Next; //Next token
 end;

The tokens returned, also include the parentheses because the definition of tokens, always includes delimiters.

### Scanning multiple lines

The exploration of several lines, consists in to explore one by one the lines of text. An exploration loop for extracting tokens in a text on multiple lines will look like this:

  //defines the syntax
  ...
  //explores
  xLex.ResetRange; //to initiate "Frange" appropriately
  for lin in SynEdit1.lines do begin
    xLex.SetLine(lin, 0); //xLex is the highlighter
    while not xLex.GetEol do begin
      //do something with the current token
      ...
      xLex.Next; //passes to the next
    end;
  end;

The current token is accessed, as usual, with GetToken() and GetTokenKind().

This sequential scanning work quite well, even for tokens that use ranges (as multiline comments) as long as it is done sequentially and the value of Frange, always keep in NIL, to start scanning[8]. It is therefore advisable, for safety, to execute ResetRange() before scanning.
[8] The highlighter could leave fRange to a value of NIL, if a previous scan, finished processing a token of several lines as a comment.

If we want to avoid having to load the entire text in a SynEdit, to begin to explore the most appropriate solution would be to use a TStringList object to store the text to explore and then work on that TStringList, as shown in the following code :

  lines := TStringList.Create;
  lineas.Text:='In place of the world,'+LineEnding+
        'Whose name'+LineEnding+
        'I do not want to remember.';
  //explores
  xLex.ResetRange; //to initiate "Frange" appropriately
  for lin in lineas do begin
    xLex.SetLine(lin, 0); //xLex is the highlighter
    while not xLex.GetEol do begin
      //do something with the current token
      ...
      xLex.Next; //passes to the next
    end;
  end;
  lineas.Destroy;

This exploration is not done on any SynEdit, but on a StringList, so that is relatively independent of SynEdit (except that it always will be required to compile the package SynEdit). On the other hand, anytime, we can "paste" the lexer to a SynEdit to see how the tokens are painted, for testing.

This exploration work well, because it is done sequentially, so that you do not need careful handling ranges (GetRange and SetRange methods).

### Random access to text

We can access any line of text directly at any time to extract containing tokens, but as long as it meets any of the following conditions:

- There is no multiline tokens in all the content (fRange always point to NIL).
- There are multi tokens, but the line that is accessed, will not contain, even partially, a multiline token.

If any of these conditions are met, the random scan of anywhere on text, is possible. We could just call SetLine() with the line we wish to explore, and advance to the desired token.

But if our syntax provides multi tokens (such as multiline comments) then the random access is not so simple.

Suppose we apply the previous scan to a hypothetical multi-code elements. The code includes multiline comments:

//sample code
{
  x = x + 2;
  c = "Hello World";
  /* This is a
  comment
  several lines */
}

If we set our highlighter, with a syntax for this language, extracting tokens might look like:

Comment : //sample code
Symbol : {
Space :
Identifier : X
Space :
Symbol : =
Space :
Identifier : X
Space :
Symbol +
Space :
Number : 2
Symbol :;
Space :
Identifier : C
Space :
Symbol : =
Space :
String "Hello World"
Symbol :;
Space :
Comment /* This is a
Comment : comment
Comment : several lines */
Symbol :}

We can see that the multiline comment is extracted as three tokens, as expected it. The proper functioning of this simple loop exploration, is given why a sequential scan is done, and tokens that handle ranges work well because it is correctly using the variable "fRange" of the highlighter.

Even the blocks information, will be handled correctly, if blocks are defined in the highlighter. So you can climb a little beyond the lexical level and reach the syntactic level.

The key is in the sequential scanning. from start to finish. So it's always correctly updated the value of "fRange".

But if we wished to perform a scan that will not necessarily sequential, and directly access the text line 6 (which is the second line a comment multiline), then we will be in the same problem in SynEdit found when exploring its contents.

The solution would be to use the same technique that performs SynEdit, which is basically:

- First perform a sequential scan of the entire text content.
- At the end of each line, store the value of Frange (in a table that has an entry for each line)

Now when we want to access randomly anywhere in the text, we must first read “fRrange” of the previous line and put it as the initial value of fRange (unless we are in the first line) at the beginning of the line.

If we do not want to complicate with "fRange" we could simply use a SynEdit editor, and use it as a text container for our lexical analyzer, leaving it to take care of managing "fRange". Then you just have to use the access functions as SetHighlighterAtXY() or GetBlockInfoAtXY() to obtain the necessary information from somewhere in the text.

Use SynEdit as container, gives us the additional advantage that we can "see" the real lexical analyzer, coloring text content.

However, it may be too heavy, use all the SynEdit to perform lexical analysis, especially if this is to be performed on various files (should always be loaded each file in a SynEdit before analysis).

Moreover, the language setting for a lexical analyzer (aimed at quickly identifying tokens) is not necessarily the best settings for a syntax highlighter (aimed at facilitating the understanding of the code by the user). It may be desirable, to have two SynFacilSyn highlighters available, one for the lexer and one for syntax highlighting.

To implement this solution, it would be best to use a TStringList to store the text to explore.

The advantage of using a TStringList, is that we can use the extra field that holds for each line, like a space to store the value of "fRange" and thus implement random access.

The following code shows how to perform the process described:

procedure TForm1.Button3Click(Sender: TObject);
var
  lin: String;
  lines: TStringList;
  i: Integer;
begin

  ///////////Create content
  lines : = TStringList.Create;
  lineas.Text: = '//example code '+LineEnding+
        '{'+LineEnding+
        ' x = x + February;'+LineEnding+
        ' c = "Hello World";'+LineEnding+
        '/ *This is a '+LineEnding+
        ' comment '+LineEnding+
        ' multiline * /'+LineEnding+
        '}'+LineEnding+'';

  ///////////performs the first scan
  xLex.ResetRange; //to initiate "Frange" appropriately
  for i:=0 to lineas.Count-1 do begin
    lin := lines[i];
    xLex.SetLine(lin, 0); //"XLex" is the highlighter
    while true do begin
      if xLex.GetEol then begin
        lineas.Objects[i] := TObject(xLex.Range);
        break;
      end;
      //you can use to do something in this exploration
      xLex.Next; //passes to the next
    end;
  end;
  //Make random access to line 6
  xLex.ran: =TPtrTokEspec(lineas.Objects[4]); //range retrieves previous line
  xLex.SetLine(lines[5],0); //assigns string
  //Here we are in line 6 and we can explore normally.
  //We will find a unique token of comment type.

  lineas.Destroy;
end;

Of course, if we want to access only once to a specific position, it would be better to explore sequentially until the desired line. But we are assuming that we are going to accessed several times to random different positions of the text.

It can be seen that for access to any line, we must first load the value of "fRange" from the previous line. This ensures a correct interpretation of the tokens.

The property "Range" of TsynFacilSyn let us to access to the internal “fRange” field.

It is assumed that the syntax is already loaded on the highlighter "xLex", and it has been defined delimiters /* and */ as multiline comments.

With this mechanism we are ensuring proper access tokens anywhere in the text, keeping the correct value of fRange. But we are not keeping the information of block.

## Tools for lexical analysis

The highlighter TSYnaFacilSyn, provides some functions that can help implement lexical or syntactic analyzers. These are:

Public //Utilities for lexical analysis
  function GetX: Integer; inline; //Current X posición of highlighter
  function GetY: Integer; inline; //Current Y position of highlighter
 function GetXY: Tpoint; //return the current position of highlighter
   property Range: TPtrTokEspec read fRange;
   property State: TFaLexerState read GetState write SetState;

If in the middle of an exploration of text, you want to know the current position being scanned, we must use the functions GetX(), GetY() or GetXY(), which can obtain the current position of the highlighter scanning.

The positions, both horizontally and vertically, always start at the value 1 for the first row or column.

For these functions to work properly, it is necessary to have correctly specified the value of "LineNumber" parameter when it was called setline(). This value starts at 0 line to the first line.

The "Range" property, as already indicated, accesses the "fRange" property that is the internal variable where the current range is saved, while a scan is performed.

The State property, allows to read or write, the internal status variables of the highlighter at any time of the scan. It returns a record of type TFaLexerState:

TFaLexerState = record
  //properties set at the beginning of the line and maintain for all the line.
  LineText : string; //workimg line
  LineIndex: integer; //current line number
  //properties that change through the line scanning
  posTok : integer; //identify the order of a token in the line
  BlkToClose: TFaSynBlock; //flag to postpone the closure of a block
  posIni : Integer; //index to the start of a token
  posFin : Integer; //index to the end of a token
  fRange : ^TTokSpec; //to work with multiline tokens
  fTokenID : integer;  //current token ID
end;

These fields are practically, all we need to read from the highlighter to determine their current status.

The most common use is when in the middle of a scan, you want to save a special position within the text and then recover it, in a more advanced state of exploration.

# For developers
## Method table

The method table is an internal structure of the highlighter used to quickly identify each element of the syntax. This structure is a prefix table, which allows using the first character of a string to quickly pass control to a processing routine (method) so you can determine the type and extent of token examined.

The table is an array of pointers to cells with 256 processing routines. This table has the following statement:

  TProcTableProc = procedure of object;
  ...
  TSynFacilSyn = class(TSynCustomHighlighter)
  private
    ...
    fProcTable : array[# 0 .. # 255] of TProcTableProc; //Method Table
    ...
  end;

This table is modified when identifiers, tokens by content, or delimited tokens, are defined, by pointing to the appropriate routines that perform the identification of tokens. This will avoid comparisons and the response speed is improved.

The methods table is started with ClearMethodTables():

procedure TSynFacilSyn.ClearMethodTables;
var i: Char;
begin
  ...
  for i: = # 0 to # 255 do
    case iof
      //white characters are fixed
      # 1 .. # 32 : fProcTable [i] : = metSpace;
      //EOL
      # 0 : fProcTable [i] : = metNull;
      else //other characters (alphanumeric or not)
        fProcTable [i] : = metSymbol; //symbols are considered
    end;
end;

The routines metSpace(), metNull() and metSymbol(), are responsible for recognizing tokens Space, End of Line and Symbol respectively. This is the definition with the highlighter starts working[9]. For safety, it's required that all characters have an associated method.
[9] Actually, the highlighter also creates a default definition for identifiers to start.

From this basic configuration, it is changing the method table so that it conforms to the syntax of work.

To put the highlighter in this initial state we call the following code.

  hlt1.ClearSpecials;
  hlt1.ClearMethodTables;

This empty syntax would only consider three types of tokens: symbols, spaces and nulls. As null tokens are found only in the end of line, then all other symbols or spaces are considered. One way to see the distribution in the method table would be:

The spaces have a fixed definition and can not be changed, which is why there will always be this category.

The symbols are not defined, are assumed to be characters that can not be processed like any other token. In a case of empty syntax, are considered like symbols, all tokens that are no spaces or nulls.

The following example shows what the initial distribution of tokens in a text with highlighter without starting:

The light gray part represents the symbol tokens type, there are 3 of them. There are also 2 tokens of type space and two Nulls, one at the end of each line.

When we start creating delimiters, delimited tokens and tokens by content, we will begin to reduce the number of characters that are considered as symbols.

## Defining identifiers

By the way is designed to highlighter, the first elements to create, should be the identifiers (which are tokens of content), because the definition of other elements of syntax may require use identifiers as part of its definition. The following hierarchy diagram, can help us to understand what is said:

The identifiers are at the same level as symbols, because both can be used as delimiters, but not any symbol or identifier. These must be special symbols or special identifiers.

A more complete diagram could be this:

The delimiters can be used in the definition of tokens, which is why they appear before.

The identifiers are defined in a simple way (to process them quickly). Externally, are defined as any token by content, but internally have restrictions such as:

- The definition must always be two lists: One for initial and one for the following characters. No more complex definitions are supported.
- Only support a list of valid characters as the first character. No strings or delimiters allowed (delimiters these are top identifiers hierarchy).
- The initial character can not be any character. They are restricted to a smaller set for design issues, to quickly process the special identifiers.

The initial list of characters, falls directly within the method table, ie it does not occupy additional space, but for the following characters are required to use a special table within the highlighter. This table has the shape of a character map:

    CharsIdentif: array[# 0 .. # 255] of ByteBool;

When we want to define a character to be part of the “valid characters for the content of identifiers”, then the corresponding box will be set to TRUE. This character map allows us to perform quick searches. Graphically we will denote it as:

As an example, consider that we define identifiers using:

  hlt1.DefTokIdentif('[$A-Za-z_]','[A-Za-z0-9_]*');

Our chart will look like this:

With this configuration, each time a character that is on the list of initial characters for an identifier is detected, it is called the metIdent() routine, which is responsible for obtaining the following characters using the map CharsIdentif:

procedure TSynFacilSyn.metIdent;
//Processes the current identifier
begin
  inc(endpos);
  while CharsIdentif [Fline [endpos]] do inc(endpos);
  fTokenID : = tnIdentif; //common identifier
end;

Once defined the identifiers, can then define the special identifiers. This definition may change references in the method table.

The symbols need not be defined, because they have a default definition, but special symbols if need be explicitly defined (except when automatically defined in the definition of other tokens or blocks).

## Special Tokens

The "special" adjective for a token should not be taken in its real meaning. Perhaps the more appropriate name would be "specialized".

Are considered special tokens:

- Special Symbols. - Is a subset of all possible symbols.
- Special Identifiers .- Is a subset of identifiers.

Both types have in common that are stored in the same data structure. What sets them apart is the way it is defined in the source text.

The special identifiers are used to store identifier of delimiter type, but can also be used to store subsets of identifiers with particular attributes (Reserved Words, constants, etc), since by default all identifiers belong to the predefined type: tnIdentif.

The situation is similar special symbols. They are used to store delimiters of symbol type, but can also be used to store subsets of symbols with particular attributes (eg operators), since by default, all symbols belong to the predefined type : tnSymbol.

The following table summarizes the statement:

SPECIAL TOKEN	TYPE OF TOKEN	FUNCTION
Special Identifier	tnIdentif	Identifiers other than tnIdentif (Keywords, Constants, ...) / Delimiter.
Special Symbol	tnSymbol	Symbols other than tnSymbol (Operator, ...) / Delimiter.

The special identifiers are stored in various tables, one for each initial character using. Currently we have the following tables:

//tables for special identifiers
mA, mB, mC, mD, mE, mF, mG, mH, mI, mJ, mK, mL, mM, //to uppercase
mN, mO, mP, mQ, mR, mS, mT, mU, mV, mW, mX, mY, mZ,
mA_, MB_, mc_, MD_, Me_, mF_, MG_, mH_, mI_, MJ_, mK_, mL are MM_, //lowercase
MN_, mO_, MP_, mQ_, Mr_, MS_, mt_, mU_, mV_, mW_, mX_, MY_, mZ_,
m_, mdol, Marr, mPer, mAmp, mC3 : TArrayTokEspec;

Multiple tables are used, to optimize the search, because it is common to have many special identifiers.

Special symbols are stored in the table mSym[], declared as follows:

    mSym : TArrayTokEspec; //table of special symbols

Only one table is used for the special symbols, because it's not expected to have defined so many symbols. Otherwise, we could create several tables in order to speed the searches.

TArrayTokEspec, is an arrangement of elements TtokSpec type:

  TArrayTokEspec = array of TtokSpec;

Is a structure used to store identifiers or symbols, and further, to store information about the properties of a delimiter. Does not mean that all identifiers or special symbols are delimiters, but when they are, here keep their properties.

The TtokSpec structure has the following declaration:

TTokSpec = record
  txt : string; //keyword
  TokPos: integer; //Token position within the line
  ttok : integer; //token type
  typDel: TFaTypeDel; {Indicates whether the current special token is,
        the starting delimiter of a delimited token}
  dEnd : string; //end delimiter (if it delimiter)
  pRange: TFaProcRange; //procedure to process the token or range(if multiline)
  folTok: boolean; //indicates whether the token delimited, has folded
  //handling properties and bending code block
  openBlk : boolean; //indicates whether the token is starting of folding
  BlksToOpen: array of TFaSynBlock; //list of references to blocks that opens
  closeBlk : boolean; //indicates whether the token is to block folding
  BlksToClose: array of TFaSynBlock; //list of references to blocks that closes
  OpenSec : boolean; //indicates whether the token is starting of section
  SecsToOpen: array of TFaSynBlock; //blocklist which is the beginning of section
  firstSec: TFaSynBlock; //section to be open when the block opens
end;

The "typDel" field shows whether the identifier or symbol or a delimiter, and if so, what type belongs. Type "TFaTypeDelim" has the following statement:

TFaTypeDelim = (
        tdNull, //not defined
        tdUniLin, //starting delimiter is delimited token of a line
        tdMulLin, //Initial delimiter token is defined multi
        tdConten1, //is starting delimiter token of Contents 1
        tdConten2, //is starting delimiter token of Contents 2
        tdConten3, //is starting delimiter token of Contents 3
        tdConten4); //is starting delimiter token of Contents 4

A token is considered as a text with a single attribute. As a token can occupy one or more lines are considered separate types to speed up processing.

This definition is oriented processing delimited tokens. But tokens also applies for content. There is a label for each token of content available.

Delimiters tokens can be grouped according to the following table:

VALUE	TYPE OF TOKEN	NUMBER OF TOKENS	NUMBER OF LINES
tdUniLin	Token uni-line	One	One
tdMulLin	Token multiline	One*	One or more
tdConten1	Token uni-line	One	One
tdConten2	Token uni-line	One	One
tdConten3	Token uni-line	One	One
tdConten4	Token uni-line	One	One

(*) When the token spans multiple lines, is composed of several tokens, because the tokens processing is done line by line.

## Detection of Special Identifiers

When special identifiers are created, the entries in the methods table are modified, in order to point to the method corresponding to the initial letter of the identifier.

Suppose we add the special identifier 'PASCAL' in our methods table:

  hlt.AddIdentSpec('PASCAL', hlt.tnKeyword);

By adding special identifiers, some entries of the table, that previously pointed to metIdent(), are updated:

As the special identifier starts with the letter "P", entries to the method metP() are added in the positions"P" and "p", assuming that the highlight is on the way of ignoring the case. If set as CaseSensitive = TRUE, the entries would point to different methods.
The method metP() is one of several similar methods exist for each possible initial letter for identifiers:

 //methods for specials identifiers
  procedure metA;
  procedure metB;
  ...
  procedure metY;
  procedure metZ;
  procedure metA_;
  procedure metB_;
  ...
  procedure metY_;
 procedure metZ_;
 procedure metUnd;
 procedure metDol;
 procedure metArr;
 procedure metPer;
 procedure metAmp;
 procedure metC3;.

There are as many methods of this type as valid starting characters that exist for identifiers. All of them have the form:

procedure TSynFacilSyn.metP;
begin
  metIdentEsp(mP);
end;

The method metIdentEsp() is similar to metIdent(), but makes a further comparison of the extracted identifier, to see if in exists in the corresponding table of special identifiers.

For each method, there is a table where the search is performed:

//tables for special identifiers
mA, mB, mC, mD, mE, mF, mG, mH, mI, mJ, mK, mL, mM, //for upper case
mN, mO, mP, mQ, mR, mS, mT, mU, mV, mW, mX, mY, mZ,
mA_,mB_,mC_,mD_,mE_,mF_,mG_,mH_,mI_,mJ_,mK_,mL_, mM_, //for lower case
mN_,mO_,mP_,mQ_,mR_,mS_,mT_,mU_,mV_,mW_,mX_,mY_, mZ_,
m_, mDol, mArr, mPer, mAmp, mC3 : TArrayTokEspec;

### Detection of Special Symbols

The case of the special symbols is similar, except that there is only one table to store:

    mSym : TarrayTokEspec;

Actually, there is an extra temporal table:

  mSym0 : TarrayTokEspec;

That is used as a intermediate storage space, before to be transferred to mSyn[].

By creating special symbols, the methods table also changes, but the process is different. Suppose we create a special symbol "+":

  hlt.AddSymbSpec('+', tnOperator);

When calling to AddSymbSpec(), does not change immediately the method table, but a new record TTokSpec is created in mSym0[].
Then, we must call the method Rebuild() to analyze the table of special symbols mSym0[] and creates the necessary entries in the methods table to process the quickest way to the special symbols.
For example, in our sample definition, the "+" symbol, should be processed making the entry "+" of the methods table, point to the method metSimbEsp(), who is in charge of detecting special symbols when find that a character can be the start of a special symbol.

But Rebuild(), will verify if it is possible to avoid the call to metSimbEsp() trying to use faster methods such as metSym1Car().
Rebuild(), also will optimize the processing of delimited tokens and tokens by content, wherever possible.

## Definition of Other Token Types

Besides identifiers (which are a special case of token), token types that exist are:

- Tokens by Contents
- Delimited Tokens.

Tokens by defining content requires additional data structures used. Therefore, you only have a fixed amount of tables contained within the highlighter[10]. There are only 5 slots reserved for managing tokens for content.
[10] These tables can be created dynamically, but require further programming and possibly affecting the speed performance.

The category of “identifier” has a space reserved in the highlighter (such as token by contents), to be important in most syntax[11]. This workspace has the advantage of enabling fast searches, for special identifiers (such as reserved words) that can not be done in other definitions of tokens for content.
[11] No mean you can not create definitions of identifiers as defined tokens, for example, but is expected tokens identifiers as defined by content.

Delimited tokens have no pre-defined spaces for storage, you can create many of them, provided there is available characters in Table Methods.

When identifiers are defined, the special area reserved for identifiers are used, and begins to consider these new types of tokens.

The unused tokens by contents will be empty sets, were not used or processed.

When additional tokens by content are defined, such as numbers, will begin to use any of the additional spaces:

  hlt1. DefTokContent('[0-9]','[0-9]*' tnNumber);

We can also add delimited tokens definitions:

  hlt.AddTokenString('','', hl.tnString);
  hlt.AddTokenString('"','"', hl.tnString);
  hlt.Rebuild;

Now the diagram might look like this:

If we also define some special identifiers, then subsets of identifiers are created with different attributes (unique identifiers).

Only the identifiers block, supports subsets with different attribute. The other blocks of content or delimited not let you manage subsets.

But we can create subsets of symbols:

  hlt.AddSymbSpec('+', tnExtra1);
  hlt.AddSymbSpec('-', tnExtra1);

As we go adding more items to the syntax, we will be completing the diagram. A more complete syntax might look like the one shown:

In this diagram, the green area corresponds to the delimiters, which as we can see, can be identifiers or special symbols. The symbols are "surplus" elements in syntax, but we can make them to be token delimiters.

All delimiters must be special symbols or special identifiers. An unusual case is to use a special identifier as comment delimiter, but this case exist in the language of DOS, where the keyword REM specifies a comment.
When a symbol or special identifier, becomes delimiter token loses its nature and become part of a larger token.

### Detection of Tokens by Content

Tokens by Content are created using the method DefTokContent():

  hlt.DefTokContent('[0123456789]', '[0123456789]*', hlt.tnNumber);

And when a token by content is defined, a new element TTokSpec, is created in the table mSym0[].

The method table is not directly modified, until Rebulid() is called, who will see if it generates a quick entry into the method table, or call the general routine metSimbEsp(), which is slower process.

The fast routines that can be introduced into the method table are:

metTokCont1();
metTokCont2();
metTokCont3();
metTokCont4();

These fast routines are introduced in the methods table when it's possible to determine, only using the first character, that we have a token by content.

Let's consider this definition:

  hlt.DefTokContent('[0-9]', '[0-9]*', '', hlt.tnNumber);

If there are no simplification, the methods table would have the next form:

But as the first character, is enough to know that we are at the start of a token by content, we can make simplifying, saving the unnecessary comparison that would make metSimbEsp(). Then we prefer to call to metTokCont1(). That is why Rebuild() directly generate entries in the methods table:

In this way, it's possible to have a faster processing.

In this example, we assume that metTokCont1() is called, because it is the first definition of token by content that is made, otherwise we could be using metTokCont2() or metTokCont3() or metTokCont4(), whichever is found free.
Furthermore, we assume that the simplification can be performed because, no other definition begins with any of the same numerical characters, exists. Consider that we have these definitions:

  hlt.DefTokContent('Ox', '[0123456789]*', tnHexa);
  hlt.DefTokContent('[0123456789]', '[0123456789]*', hlt.tnNumber);

Under this scheme, simplification can not be given for the character "0" because it's not enough, just this character to know what definition of token by content, belongs this token, but must do a more complete verification. In this situation, Rebuild (), would leave the method table thus:

### Detection of Delimited Tokens

Delimited tokens are defined with the method DefTokDelim:

  hlt.DefTokDelim('"','"', hl.tnString);

This definition, creates a new element TTokSpec, in the table mSym0[].

The methods table is not directly modify, but until Rebulid() is called. It is Rebulid(), who will see if it generates a quick entry into the methods table, or call the general routine metSimbEsp(), which is slower process.
Fast routines that can be introduced into the methods table are:

metUniLin1();
metFinLinea();

Fast routines are introduced in the method table when it is possible to determine, by only using the first character, that we have a delimited token.
Consider for example, the following definition:

  hlt.DefTokDelim('"','"', hl.tnString);

In this case, if there is not simplification performed, we would have this scheme:

But as the first character is enough to know that we are at the start of a delimited token, we can make simplifying, saving the unnecessary comparisons that metSimbEsp() would do, for finally call to metUniLin1(). That is why Rebuild() directly generate entries in the method table:

Thus achieving faster processing.
In this example, we assume that simplification can be done because there is not another definition of token that begins with the quote character, otherwise the simplification can not be realized.
Note that the character '"', becomes a special symbol and a boundary as a result of being part of the definition of a token by content.

## Driving Ranges

For general information on handling ranges, please read "La Biblia del SynEdit- Rev6 - Section 2.3.10" on the management ranges.

Unlike a fixed highlighter, "TSynFacilSyn" can not have fixed quantity of ranges to handle multiline syntax elements.

A fixed highlighter usually has a definition like this:

type
  TRangeState = (rsUnknown,
        rsComment, //comment
        rsComment2, //comment
        rsString); //string

However, in our highlighter, there is no such definition for the management ranks, because there can be many different ranges.

In fact, whenever a multiline token is defined, it is creating a different range. In the highlighter, the variable "fRange" is not an enumerated (as in most highlighters), but is a true pointer:

    fRange : ^ TtokSpec; //to work with multiline tokens

The reference to a record TTokSpec is done to access the fields of the special token, which defines the range. That is why TTokSpec, has full information of the block, when it is a delimiter:

  TtokSpec = record
    txt : string; //keyword
    orig : string; //keyword as real indicated
    TokPos: integer; //Token position within the line
    tTok : integer; //token type
    typDel: TFaTypeDel; {Indicates whether the current special token, is
        actually, the starting delimiter of a delimited token}
    dEnd : string; //end delimiter (if it delimiter)
    pRange: TFaProcRange; //procedure to process the token or range (if multiline)
    folTok: boolean; //indicates whether the token delimited, has folding
...
  end;

Thus, when we begin to explore multiline tokens, is assigned to fRrange, the reference to the starting delimiter record:

procedure TSynFacilSyn.ProcTokenDelim(const d: TTokSpec);
...
      fRange : = @d;
...

When no range is handled, fRange should be NIL.

In the method Next(), a check is made to see if it is in the middle of a range, and if so, the information of the targeted record will be used:

procedure TSynFacilSyn.Next;
begin
...
  posIni := endpos; //points to the first element
  if Frange = nil then begin
      Charini :=Fline [endpos]; //store to have it available in the method that will be called.
      fProcTable[Charini]; //The corresponding function is executed.
    end
  else begin
    if endpos = Tamlin then begin //to accelerate exploration
      fTokenID: =tnEol; exit;
    end;
    fTokenID: = ^fRange .tTok;
    ^fRange.pRange; //run method
  end;
end;

This "advanced" management of ranges, has an additional complication. One is to be updated necessarily information SynEdit ranges, when the syntax is changed. Otherwise we would have ranges of the lines could be pointing to nonexistent positions. This task is easily implemented by calling ScanAllRanges:

procedure TSynFacilSyn.Rebuild;
...
  Self.ScanAllRanges;
...

## Blocks and Sections

The blocks are born as a need to implement the code folding facility. However, they were created, thinking on defining syntactic special regions. Ie, highlighter blocks are oriented to represent the real syntactic blocks of the language they use.

This means that if we set the highlighter to work with a syntax in C, then the block, in braces, is not only a visual aid to apply code folding, but also that logically represents a set of instructions, which are syntactically equivalent to a single, like in C language.

This way, you can represent many structures of the language itself, using blocks and sections.

The sections with as an additional tool to enhance the ability to create special text regions. They were defined considering the structure of the Pascal language, but are rather general, to apply to different languages.

While the concept of "block" within the highlighter TSynFacilSyn is similar to the concept of "Block" (Block Fold or Fold Block), within SynEdit, it should be noted that there are some differences between these concepts:

- The blocks within the TSynFacilSyn, use machinery of SynEdit blocks to implement, but complement the functionality to extend the concept of block.
- The blocks of TSynFacilSyn are defined as special regions of several tokens, which may occupy one or more lines. SynEdit blocks, which occupy a line, are not considered (not generate fold marks).
- SynEdit blocks basically are used to implement the code folding functionality. TSynFacilSyn blocks, define regions of semantic meaning.

Internally the blocks and sections TSynFacilSyn share the same structure. Are implemented with a class:

  TFaSynBlock = class //class to handle syntax blocks
    name : string; //block name
    dStart, dEnd: string; //delimiters
    index : integer; //indicates its position within TFaListBlocks
    showFold : boolean; //indicates whether the fold mark is displayed
    parentBlk : TFaSynBlock; //parent block (where the block is valid)
    Backcol : TColor; //background color of a block
    IsSection : boolean; //indicates whether a block of type section
    UniqSec : boolean; //Indica is only section
  end;

Each new block created (or section), dynamically generates a new object TFaSynBlock. The only internal difference between a block and a section is that this is the "IsSection" field to TRUE, and therefore makes sense the "UniqSec" field.

For handling blocks, additional fields are used in the records "TTokSpec"

TTokSpec = record
...
  //handling properties and bending code block
  openBlk : boolean; //indicates whether the token is starting block folding
  BlksToOpen: array of TFaSynBlock; //list of references to blocks that opens
  closeBlk : boolean; //indicates whether the token is to block folding
  BlksToClose: array of TFaSynBlock; //list of references to blocks that closes
  OpenSec : boolean; //indicates whether the token is starting block section
  SecsToOpen : array of TFaSynBlock;//list of blocks which is the beginning of section
end;

Each, when a new section or block adds, delimiters are also added as special tokens (identifiers and symbols), if they did not exist, and block properties are configured.

Block handling management is independent tokens. Recognition of tokens is a separate task that is done by specialized routines. Blocks working on these routines, without interfering in their work.

The processing of blocks and sections, introduces an additional charge to the highlighter, but in heavy tests, could be estimated that the performance is as good (or even better) as fixed highlighters that come with Lazarus.

Note that the routine Rebuild(), can not optimize the syntax correctly, when a common symbol is, at the same time, a block delimiter. Consider for example, a block whose delimiters are parentheses. Then the symbols "(" and ")" will create special symbols with associated blocks, and have to go through all the checks (inside metSimbEsp), each time a parentheses is detected. Normally parentheses are treated as mere symbols and would process quickly. If they were defined only as special symbols, Rebuild() could optimize processing using the method table and metSym1Car() routine.

The idea to implement the folding is simple, and is based on using these three functions: StartCodeFoldBlock() EndCodeFoldBlock() and TopCodeFoldBlockType(). By the moment, it is not being used the “Fold Config” options[12] through the class "TSynCustomFoldConfig", although initially it was thought to derived "TfaSynBlock" from the class "TSynCustomFoldConfig".
[12] The folding configurations options let you save information on folding blocks that are accessible externally from public properties of the class. For more information it is recommended to see "The Bible of SynEdit - Rev 5", section about Folding Code.

The blocks are always open, calling StartCodeFoldBlock() and always close, calling EndCodeFoldBlock(), regardless whether to display or not fold mark.

Each time a special token is found, it is checked whether this is starting delimiter of a block or section (biased in section[13]), And if so proceeds to open the folding block (or simply start the block without folding, according to the configuration). To open the folding block, it first checks whether the current block or section is corresponding. Technically, the block is open after recognizing the token, however, this should open before, because the initial token is also part of the block, however, folding end (which works with lines) code no harm.
[13] The fact prioritize defining section with respect to the block, which is a characteristic defined by observations of how the code is handled in Pascal, but should be consistent with other languages.

To find the end of the block, it is checked each time is a special token, if this is the end of a block or section. Using the information from the current block or section is determined whether or not the folded closed. The fold is closed after recognizing the boundary token, and so work as expected, so the next block so no complications.

A table could help and explain the situation:

DELIMITER	TYPE	THE BLOCK OPENS ..	THE BLOCK SHOULD OPEN ..
Of Start	Symbol or identifier	After identifying the token	Before identifying the token !!!!
Of End	Symbol or identifier	After identifying the token	After identifying the token

This method works well for blocks that that have delimiter tokens defined, and the gap when opening the block, is not notorious for folding purposes.

For handling sections, however, the situation is a bit more problematic, because the sections do not have a defined end delimiter. So in theory, should be closed before identifying the start of the next section or the end of the block that contains it. However, for technical reasons the highlighter newly detected that must close the previous section, once identified the token that start the next section, which usually is on the next line, of the end of the section.

For better understanding, consider the following picture:

Looking inside, you can see that the folding of the "interface" section, extends to the line where "implementation" is, because only then, has been identified as the "interface" section is over. So we have a folding is not as consistent with the definition. Fortunately, folding machinery of SynEdit, will know not to hide this line when the fold of "interface" is closed.

So far, it has kept this "defect". But it is known that it is possible to implement more elaborate mechanisms to properly close the fold in the case of sections (as supposed highlighter Pascal Lazarus do).

## Colored blocks

The functionality of colored blocks allows us to see the physical boundaries of the blocks in the editor, but this is basically an illusion.

The Start and/or End position of the block is not stored anywhere. The highlighter does not have storage space to define blocks (such as the philosophy of work). All information regarding folding blocks (no blocks TSynFacilSyn) are saved in the highlighter, along with information of ranges, as an object associated with each line, and basically what is written here, is the state of highlighter at the end of the scan line (For more information, see “The Bible of SynEdit” in the section on TSynCustomFoldHighlighter).

The boundaries of TSynFacilSyn blocks are defined at runtime, when the token are scanned, as highlighters have the token as the smallest unit of exploration.

To better visualize the scanning process, consider the following sequence diagram:

Drawing a complete token is performed after SynEdit call GetTokenEx() and GetTokenAttribute(). Therefore, if we want to change the attribute of the token, it must be done before returning the attribute with GetTokenAttribute().

This is the way the tokens are scanned. The logical question would be, what time they open or close the blocks? Because as implemented TSynFacilSyn, the blocks are open or closed (StartCodeFoldBlock() and EndCodeFoldBlock()), in the method Next(), because this is where it ends to "extract" the tokens of the text and can be evaluated the necessary conditions.

The following diagram shows the sequence in the opening and closing of blocks:

To achieve the colored blocks, the technique is to change the background color on the attributes of the tokens contained in a specific block[14].
[14] Unfortunately change the background attribute tokens, leading to a loss of information background color of the tokens (remains as a pendant, solving this fault).

The problem then reduces to determining, before returning the value GetTokenAttribute(), if the token belongs or not to block anyone. To do this we will intercept the method TSynFacilSyn.GetTokenAttribute() and change the background color of the token, according to the color defined for the current block background:

function TSynFacilSyn.GetTokenAttribute: TSynHighlighterAttributes;
{Must return the attribute for the current token. The current token is updated
 with each call to "Next" (or "setline" to the first token of the line.)
This function is, what usually SynEdit uses, to define the attribute of the current token}
var Topblock: TFaSynBlock;
begin
  Result : = fTokenID; //might return "tnEol"
  if Result<> nil then begin
    //colored block verifies
    case ColBlock of
    cbLevel: begin //paint by level
        Result.Background: =RGB(255- CodeFoldRange.CodeFoldStackSize*25.255- CodeFoldRange.CodeFoldStackSize*25.255);
      end;
    cbBlock: begin //paint by block type
        Topblock : = TFaSynBlock(TopCodeFoldBlockType);
        if Topblock= nil then Topblock : = MainBlk;
        Result.Background: =topBlock.BackCol;
      end;
    end;
  end;
end;

The choice of colored "cbBlock" reads the "current" block (last open block) using TopCodeFoldBlockType(). This implies that the current block, remains open (do not call EndCodeFoldBlock() until it has been called GetTokenAttribute().

Reading the initial token of a block, color block is read correctly, because the block is open, before calling TSynFacilSyn.GetTokenAttribute() (opens in Next ()). But at closing the block, for the same purpose, the read color, would correspond to the next block (See above sequence diagram).

Therefore, for colored block, we have the opposite effect, with respect to the detection of blocks (see previous section), in determining the block boundaries.

To address this gap, is that the closure of a block, is postponed until reading the next token. That is why it has been created the flag "BlkToClose", and ends to close the block on "Next"[15].
[15] We initially tried to implement the closure of the block in the same GetTokenAttribute (), after setting the color of the block, but it was verified that there were errors in coloring. No reason found why exactly...

The variable "BlkToClose" It is actually a pointer to the current block, which is expected to close. When there is not block on hold, it is NIL.

The following diagram shows how the current sequence:

As "BlkToClose" is a variable whose life should not exceed one line, it always starts in Setline().

You can then see that all machinery for opening/closing block, exists only within the method Next(). The extension of a block are not stored anywhere in TSynFacilSyn. The block has a lifetime in the text scanning process.

Colored function block uses this information to change the background color of the tokens, on the fly, when you call GetTokenAttribute().

## Blocks and Ranges

There is some interference between the management blocks, and multiline tokens (which may also have information folding). To improve this relationship, It has to be included the block "MulTokBlk" to make multiline tokens may include code folding when, and work well in a more "standard" way.

However, this implies that all types of multi tokens share a single block object, which may limit options for coloring. For example if the colored block MulTokBlk activated, this will be effective for all without distinction multi tokens, whether are strings or comments.

## Speed ​​optimization

It is known that the greatest difficulty in implementing a highlighter to SynEdit is the speed of response, and that depends on how fast it is to identify the tokens.

Optimization has been made to recognize tokens, not for construction of the syntax.

The implementation is done by optimizing the speed to the maximum extent. It's not used using "hash functions" as in most highlighters because they are not flexible configuration, and in my tests, I checked that are up slower speed (See http://forum.lazarus.freepascal.org/index.php?topic=22008.0 ).

The method used, resembles a tree prefixes, but using only the first letter to improve identification of tokens. Quick Search This method applies to both identifiers as delimiters.

Consider the special identifiers are stored in one of the 58 special tables are reserved. This separation is done to speed up the identification of specific identifiers.

The idea is to use the initial character (line analyzed), to determine quickly to routine processing token is derived (using the method table). As each routine, it's only specialized in identifying a small group of identifiers, so it can be done quickly.

To be able to quickly identify the characters that may be part of an identifier, it is used an array of Boolean values (CharsIdentif []).

Delimiter symbols are stored only on the table mSym[], and have a similar processing of identifiers (to optimize the speed). For this purpose the method table is set, so refer the processing routine delimiters (metSimbEsp) for each character that can be the beginning of a delimiter. Using a table of valid characters for an anchor (CharsIdentif) is also made.

The highlighter works according to the rules described in this document, if you modify a feature, this document should be updated.

To expand the list of characters available for the initial character of an identifier must be modified "AgregaIdenEspec" and create the appropriate method (metXXX) and create the new tables.

## Lightening the highlighter

The unit highlighter is a fairly quick and relatively light in terms of memory space code. But if you want to make it more compact, whether for performance issues or simplification, you can easily remove certain functionalities.

### Functionality "CaseSensitive".

This option requires the use of 26 more tables within the unit. If this option is not desired and only want to process tokens ignoring case, you must drop the tables:

mA_, mB_, mC_, mD_, mE_, mF_, mG_, mH_,
mI_, mJ_, mK_, mL_, mM_, mN_, mO_, mP_,
mQ_, mR_, mS_, mT_, mU_, mV_, mW_, mX_, mY_, mZ_

And also the CaseSensitive field, then go selectively removing the code that makes use of these data.

The metA_, metB_ ... methods also must be removed.

The simplest way would be to eliminate the variables listed and then compile to see what part of the code these variables are used.

In the case of "CaseSensitive" would work just because he is a Boolean variable, then would proceed to the simplification using the slogan "assume that the variable will always FALSE". For example, the following code:

If CaseSensitive then a
  {Part TRUE}
else
  {Part FALSE}

It will be like:

  {Part FALSE}

If desired, further simplification can also eliminate the variable "tCasSen" from "FirstXMLExplor" and its associated code.

After this simplification, the code should be reduced by about 100 lines. It is also believed that improved highlighter speed between 1 and about 2%.

### Management of sections

If you only want to use the handling blocks without sections, you can completely remove this functionality.

The additional code for the handling of the sections, is considerable. In addition there is an additional processing load.

To eliminate handling sections, we must first remove the properties of "TTokSpec" sections regarding "OpenSec" and "SecsToOpen". Also the properties of "TFaSynBlock" referring to sections: "IsSection" and "UniqSec". All code associated with these properties should be removed. It should also eliminate Addsection() method, and the code that processes sections LoadFromFile().

You can also remove only the characteristic of "First Section", removing the "firstSec" field of "TTokSpec" and all the associated code.

### Folding functionality.

If the code folding functionality in any form is not required, can be completely eliminated this functionality. If so, would considerably reduce the size of the unit and the additional processing load.

However, removing TSynFacilSyn, folding, is to have a highlighter of type TsynFileSyn (An old version). So instead of manually delete all the properties and methods relating to fold better TSynFileSyn should use the highlighter, which is quite lighter.

### Reading XML file

In the unlikely case that is not going to set the highlighter using the XML file, and only desired to do so by instructions. You can remove all heavy machinery reading syntax file.

To begin, you must remove FirstXMLExplor() and LoadFromFile().

It should also eliminate TFaXMLatrib types and functions LeeAtrib(), IsAttributeName() and ValidateAtribs() because they would no longer be necessary.

The code is considerable saving of about 300 lines. The processing speed is not affected, because the main routines are not modified.

## Limitations

The highlighter makes a compromise between speed and flexibility. Because of this, there are some trade-offs:

1. Only is permitted to define four tokens by content, in addition to the space reserved for identifiers. Creating more, it is easy, and only slightly loaded memory.
2. You can not create subsets of tokens, for other tokens by content than are not identifiers or symbols.
3. Block delimiters can not be of type "<identifier> <space> <identifier>". For example, you can not define "END IF" as delimiter block.
4. The sections can not contain other sections. Currently the sections can only contain blocks, but no big problem.
5. The handling of UTF-8 is still limited in the highlighter.
## Pending improvements

There is always room for improvement. Listed are just a few that were always in mind when the highlighter was developed.

- Correct the limit of the fold mark for sections (See 6.6 - Blocks and Sections). Currently folding extends to a line after the end of the section.
- Deactivate the colored blocks, without creating new highlighter. Currently, when the colored block is activated, the background color information of all tokens are lost.
- Creating nested sections.
- Ability to define a special block for multiline tokens with folding support. Currently all multiline tokens share the same block "MulTokBlk".
- The definition of identifiers and special identifiers in UTF-8 can be improved.

# Content